# MEDIUM HEAVY-DUTY TRUCK TEST CYCLE EVALUATION

# Final Report

# CRC Project No. E-55-3

# February 2004

Prepared  for:

### California Environmental Protection Agency

Air Resources Board

1001 I Street - Sacramento, California 95814

and

Coordinating Research Council, Inc.

3650 Mansell Road, Suite 140  -  Alpharetta, Georgia 30022

# MEDIUM HEAVY-DUTY TRUCK TEST CYCLE EVALUATION

# Final Report

# CRC Project No. E-55-3

Submitted by:

West Virginia University Research Corporation

886 Chestnut Ridge Road

P. O. Box 6845

Morgantown, WV  26506

Prepared by:

Nigel N. Clark and Mridul Gautam (Principal Investigators)

W. Scott Wayne and Donald W. Lyons (Co-Principal Investigators)

National Center for Alternative Fuels, Engines and Emissions

Department of Mechanical and Aerospace Engineering

West Virginia University

Morgantown, WV  26506-6106

# February 9, 2003

CRC E55-3: Medium Heavy-Duty Truck Test Cycle Evaluation

# TABLE OF CONTENTS

TABLE OF CONTENTS	iii

LIST OF FIGURES	iv

LIST OF TABLES	v

EXECUTIVE SUMMARY	vi

INTRODUCTION AND PRESENTATION OF MHDT SCHEDULE	1

OBJECTIVE	4

ANALYSIS OF MHDT SCHEDULE	4

PROCUREMENT OF TEST VEHICLES	6

TEST APPARATUS	8

PRELIMINARY TEST RUNS	8

EMISSIONS DATA – STANDARD TRANSMISSION VEHICLE	13

EMISSIONS DATA – AUTOMATIC TRANSMISSION VEHICLE	21

COMPARISION WITH DATA FROM THE UDDS (TEST_D)	23

CONCLUSIONS	23

REFERENCES	25

APPENDIX A: MHDT Schedule	26

APPENDIX B: Emissions data from this evaluation program.	28

# LIST OF FIGURES

Figure 1 The Lower Speed Transient Mode of the MHDT Schedule.	2

Figure 2 The Higher Speed Transient Mode of the MHDT Schedule.	3

Figure 3 The Cruise Mode of the MHDT Schedule.	3

Figure 4 GMC truck with 6 speed manual transmission.	7

Figure 5 Freightliner truck with automatic transmission.	7

Figure 6 Photograph of a portion of the medium-duty chassis dynamometer. The flywheel set is on the left, the power absorber is right of center, and two of the rollers are seen on the extreme right.	9

Figure 7 Target speed and actual speed versus time for the Lower Speed Transient mode (6077-1) using the standard transmission vehicle at laden weight.	10

Figure 8 Target speed and actual speed versus time for the Higher Speed Transient mode (6077-2) using the standard transmission vehicle at laden weight.	10

Figure 9 Target speed and actual speed versus time for the Cruise mode (6077-3) using the standard transmission vehicle at laden weight.	11

Figure 10 Actual speed versus target speed for the Lower Speed Transient mode (6077-1) using the standard transmission vehicle at laden weight.	11

Figure 11 Actual speed versus target speed for the Higher Speed Transient mode (6077-2) using the standard transmission vehicle at laden weight. The string of points highest above the parity line represents a failure to brake as quickly as the target trace commands.	12

Figure 12 Actual speed versus target speed for the Cruise mode (6077-3) using the standard transmission vehicle at laden weight. Most points below the parity line correspond to the vehicle lagging an acceleration ramp.	12

Figure 13 NOX versus time for unladen run and laden run on the Lower Speed Transient mode.	18

Figure 14 NOX versus time for unladen run and laden run on the Higher Speed Transient mode.	19

Figure 15 NOX versus time for unladen run and laden run on the Cruise mode.	19

Figure 16 CO versus time for unladen run and laden run on the Higher Speed Transient mode.	20

Figure 17 HC versus time for unladen run and laden run on the Higher Speed Transient mode.	20

Figure 18 NOX versus time for the Lower Speed Transient mode for the automatic truck (run 6108-4).	22

Figure 19 NOX versus time for the Higher Speed Transient mode for the automatic truck (run 6109-2).	22

Figure 20 NOX versus time for the Cruise mode for the automatic truck (run 6112-2).	23

# LIST OF TABLES

Table 1: Summary Statistics for the MHDT Data Set.	2

Table 2 Analysis parameters for the as-received Lower Speed Transient, Higher Speed Transient and Cruise modes of the MHDT schedule.	4

Table 3 Analysis parameters for four HHDDT, CSHVC and Highway mode.	5

Table 4 Vehicle information of the MHDT with manual transmission	6

Table 5 Vehicle information of the MHDT with automatic transmission	6

Table 6 Analyzer used for regulated gases and carbon dioxide	8

Table 7 Data from preliminary runs on the standard transmission GMC vehicle at laden weight. Units are g/mile	9

Table 8 Emissions data on laden test runs for the sequence numbers 6076, 6077, 6078 and 6081. Where there are only two runs, statistics show the difference and difference/average values. Absent PM values are due to a filter weighing error detected during data processing.	13

Table 9 Emissions data for laden test runs for the sequence numbers 6104 and 6105.	15

Table 10 Emissions data from the GMC truck on laden test runs for the sequence numbers 6082, 6083 and 6084.	16

Table 11 Emissions data on unladen test runs for the sequence numbers 6098, 6099, 6100 and 6101. Units are g/mile. Data are shown from only the primary NOX analyzer.	17

Table 12 Fuel consumption and NOX increase from unladen (50% GVW) to laden (90% GVW) test runs for the three modes with the GMC vehicle.	18

Table 13 Emissions data from the automatic Freightliner truck.	21

# EXECUTIVE SUMMARY

A Medium Heavy-Duty Truck (MHDT) schedule, developed by the California Air Resources Board (ARB), was examined experimentally to determine its suitability as a future research tool. The MHDT was developed to aid in emissions characterization of trucks with 14,001 to 33,000 lb. gross vehicle weight, exercised on a chassis dynamometer.  This weight range encompasses a wide variety of vehicles, with varying power to weight ratios and with synchronized manual, unsynchronized manual, and automatic transmissions.  A major objective of this program was to examine repeatability of emissions data from MHDT driven through this schedule. The MHDT schedule consisted of three modes; namely, a Lower Speed Transient, a Higher Speed Transient, and a Cruise mode. The maximum speeds of these modes were 28.9, 58.2 and 66.0 mph, respectively.

Two trucks were procured to acquire emissions data using the MHDT schedule. The first, a 2000 model year (MY) GMC truck with a 8.2 liter Isuzu engine and a synchronized standard transmission, was tested at a laden weight (90% GVW, 17,550 lb.) and at unladen weight (50% GVW, 9,750 lb.). The second, a 1999 MY Freightliner with a 7.2 liter Caterpillar engine and an automatic transmission, was tested only at 13,000 lb. (50% GVW). The test runs were performed using the West Virginia University (WVU) medium-duty chassis dynamometer, located in Riverside, CA. Vehicle inertia was mimicked using a flywheel set, and tire and wind drag were mimicked using an eddy current power absorber. The truck exhaust was ducted to a full-scale dilution tunnel, with HEPA filtered dilution air, and a flow rate of approximately 1,500 scfm. Particulate matter (PM) mass was found gravimetrically, using filtration, while carbon dioxide (CO2), carbon monoxide (CO), oxides of nitrogen (NOX) and hydrocarbons (HC) were measured using research grade analyzers. Test protocols were the same as those developed previously for the ARB Heavy Heavy-Duty Diesel Truck (HHDDT) schedule. Data were computed in units of g/cycle, g/mile, g/ahp-hr, g/gallon and g/minute, and were examined most carefully in units of g/mile.

Maximum acceleration rates (of 4.6 to 5.5 mph/s) in the modes of the MHDT were high for the GMC vehicle when the vehicle was laden.  This can be attributed to both the power to weight ratio and the time needed to shift gears with a manual transmission.  Preliminary runs showed that the GMC truck did deviate from the target trace when tested at laden weight, and the completed distance for the MHDT Lower Speed Transient mode (which has a high maximum acceleration of 5 mph/s) varied from 0.906 to 0.954 miles, compared to a target distance of 0.963 miles.

Averaged GMC truck emissions results for a final set of three repeat laden runs are shown in the following table:-

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower speed Transient | Ave. | 2.78 | 9.23 | 0.56 | 1370 | 0.25 |
|  | Std. Dev. | 0.23 | 0.12 | 0.02 | 70 | 0.01 |
|  | CV% | 8.2 | 1.3 | 3.6 | 5.2 | 4.8 |
| Higher Speed Transient | Ave. | 1.73 | 6.83 | 0.33 | 1087 | 0.21 |
|  | Std. Dev. | 0.10 | 0.12 | 0.03 | 41 | 0.04 |
|  | CV% | 6.0 | 1.7 | 9.6 | 3.8 | 17.3 |
| Cruise | Ave. | 0.82 | 5.07 | 0.18 | 655 | 0.09 |
|  | Std. Dev. | 0.01 | 0.15 | 0.01 | 4 | 0.00 |
|  | CV% | 0.7 | 3.0 | 3.2 | 0.6 | 2.5 |

Unladen data from the GMC truck on a set of four repeat runs are presented in the following table:-

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower speed Transient | Average | 2.79 | 7.88 | 0.53 | 1116 | 0.21 |
|  | Std Dev | 0.24 | 0.27 | 0.01 | 46 | 0.04 |
|  | CV% | 8.6 | 3.5 | 2.5 | 4.2 | 19.6 |
| Higher Speed Transient | Average | 1.56 | 5.49 | 0.29 | 811 | 0.15 |
|  | Std Dev | 0.08 | 0.26 | 0.03 | 35 | 0.03 |
|  | CV% | 5.0 | 4.7 | 10.1 | 4.4 | 16.5 |
| Cruise | Average | 0.90 | 4.44 | 0.19 | 598 | 0.09 |
|  | Std Dev | 0.07 | 0.12 | 0.00 | 12 | 0.01 |
|  | CV% | 8.1 | 2.7 | 1.7 | 2.2 | 7.3 |

When the GMC truck test weight was reduced from laden to unladen, reductions of carbon dioxide (as an indicator of fuel consumed) and of NOX and PM emissions were modest in comparison to prior data for HHDDT. This can be explained because vehicle inertia has proportionally less influence on engine load in MHDT than HHDDT.   For the GMC laden and unladen runs, the percent variability (CV%) for NOX was less than 5% for all runs, and averaged at 2.8%.  This NOX CV% is deemed to represent good repeatability by the investigators.  For PM the average was 11.3%, which is acceptable, noting the sensitivity of PM production to driving variations and noting the variability associated with PM capture, filter weighing, and background correction.

The Freightliner, with an automatic transmission, produced the following emissions:-

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower Speed Transient | Average | 3.55 | 16.39 | 0.49 | 1662 | 0.33 |
|  | Std Dev | 0.09 | 0.19 | 0.01 | 17 | 0.01 |
|  | CV% | 2.5 | 1.2 | 2.8 | 1.1 | 3.6 |
| Higher Speed Transient | Average | 1.93 | 12.59 | 0.35 | 1222 | 0.25 |
|  | Std Dev | 0.05 | 0.22 | 0.01 | 15 | 0.01 |
|  | CV% | 2.6 | 1.8 | 3.6 | 1.3 | 4.6 |
| Cruise | Average | 1.19 | 7.9 | 0.34 | 1101 | 0.14 |
|  | Std Dev | 0.04 | 0.30 | 0.02 | 28 | 0.02 |
|  | CV% | 3.1 | 3.7 | 4.7 | 2.6 | 11.4 |

Repeatability of NOX and PM data on the Freightliner were better than for the GMC truck.  Based on overall data repeatability, the investigators have concluded that the MHDT is suitable for characterizing the emissions from trucks in future inventory research.  Emissions Data from the MHDT were also compared with data gained using the Heavy-Duty Urban Dynamometer Driving schedule (UDDS) from CFR 40.  For the GMC truck, laden UDDS NOx data were at a similar level to data for the Higher Speed Transient Mode.  For the Freightliner truck, the UDDS NOx level was slightly lower than for the Cruise Mode.

# INTRODUCTION AND PRESENTATION OF MHDT SCHEDULE

There is a strong desire to characterize realistically the in-use emissions of heavy-duty trucks because they are known to contribute significant emissions to the inventory. Prior research [1, 2] has established that the nature of a chassis dynamometer test schedule will affect the emissions levels (usually expressed in units of g/mile) and so it is important that the schedule contains vehicle behavior that reasonably represents the behavior of trucks in real use. West Virginia University has recently conducted research, funded through the Coordinating Research Council (CRC), on Heavy Heavy-Duty Diesel Truck (HHDDT) emissions [3, 4]. This prior research commenced with an evaluation of a new test schedule (of 4 modes) for HHDDT developed by the Air Resources Board (ARB) of the State of California [5].  To meet the need to characterize emissions from Medium Heavy-Duty Trucks (MHDT), both gasoline and diesel fueled, ARB produced a new MHDT schedule, reflecting the MHDT activity data collected throughout the state of California in two prior ARB funded studies during 1997-2000. In these prior studies "randomly" selected study vehicles were fitted with data loggers equipped with Global Positioning System (GPS) receivers.  Second-by-second data were collected from a total of 140 heavy-duty trucks (HDTs) from a study performed by Battelle, and from 31 HDTs for the truck activity study conducted by Jack Faucett Associates.  These 171 vehicles spanned the domain of weight classes from light heavy-duty gasoline trucks, to heavy heavy-duty diesel trucks (HHDDTs). This 171-vehicle data set included 35 medium heavy-duty diesel trucks (MHDDTs) and five medium heavy-duty gasoline (MHDGTs) trucks. Medium heavy-duty trucks are defined as trucks with gross vehicle weights between 14,001 - 33,000 lbs. (6,342 – 14,949 kg). This category includes vehicles such as 'step vans', 'box trucks', flatbeds with one drive axle, and relatively small single-axle tractors.

The MHDDTs and MHDGTs data sets were processed and analyzed separately to see if there were significant differences between the two in terms of cycle development parameters. The two data sets were determined to be similar enough to warrant combining them into a single data set for MHDTs as a general weight class. In addition, the MHDDTs were over-sampled for the usage/business category of parcel delivery vans. As a consequence, the 23 parcels trucks comprising this usage/business category were distilled into a single vehicle that represented the aggregate statistics of this category.  Another MHDDT was eliminated from the data set due to questions regarding the veracity of the GPS data. The data indicated that this vehicle took a single trip of some 40,000 seconds (11.1 hours).  Thus, the data set used for cycle development consisted of 17 vehicles; namely, 12 MHDDTs and five MHDGTs. The final data set consisted of 720,514 records, representing about 200 hours of medium heavy-duty vehicle activity throughout the state of California.  Summary statistics are presented in Table 1.

It should be noted that the Battelle data contained a data compression routine where idle periods in excess of two minutes recorded time stamps only once every thirty seconds.  In this way some idle activity may have been lost. However, when these data were expanded, the percent idle grew by only a few percent. The data sources and the methodology for producing these modes were the same as for the previous HHDDT schedule [5]. Candidate modes were created by joining trips, and the statistical parameters describing candidate modes were compared to the database parameters to select the mode which most closely represented the database. Modes were also created to have a reasonable duration for use on a chassis dynamometer. For MHDT no idle mode was created because idle was not found to be a dominant form of operation, as was the case for HHDDT.  The new schedule contained three separate modes:

1.	Lower Speed Transient mode,

2.	Higher Speed Transient mode, and

3.	Cruise mode.

Table 1: Summary Statistics for the MHDT Data Set.

| PARAMETER |  |
| --- | --- |
| Total number of trips | 564 |
| Total time - seconds | 720,514 |
| Total vehicle miles traveled (VMT) | 5,606.4 |
| Average Speed - mph | 28.01 |
| Average trip length - miles | 9.94 |
| Average trip duration - seconds | 1277.5 |
| Stops per mile | 31.1 |
| Average maximum speed - mph | 39.2 |
| Average maximum acceleration - mph/s | 4.4 |
| Average maximum deceleration - mph/s | -4.6 |
| Total Kinetic Energy - mph2 | 340.8 |
| Percent idle | 12.8 |

Speed-time graphs of these modes were made available to WVU by ARB and are presented in Figure 1 to Figure 3. In this report, the term “MHDT Schedule” will refer to a sequence of the three “modes.” The term “cycle” has been avoided to prevent confusing the parts (modes) and the whole of the new schedule.

Figure 1 The Lower Speed Transient Mode of the MHDT Schedule: the target distance is 0.963 miles.

Figure 2 The Higher Speed Transient Mode of the MHDT Schedule: the target distance is 7.13 miles.

Figure 3 The Cruise Mode of the MHDT Schedule: the target distance is 21.26 miles.

# OBJECTIVE

The objective of this research was to evaluate the recently developed ARB MHDT truck schedule. The evaluation was to ascertain the suitability of the schedule for use with a chassis dynamometer, to acquire a set of preliminary data, and to examine repeatability of data. It was not necessary to develop new test protocols, because it was believed by ARB and by the WVU investigators that the test protocols developed previously for the HHDDT cycle [5] should be utilized for the MHDT cycle.  These protocols address the need to precondition the vehicle sufficiently to enable a hot start test, and address the soak time allowed between modes and schedules. A ten-minute soak was preferred, but the soak should not exceed 20 minutes without precipitating the need for a new conditioning cycle or mode. The protocols also call for 30 to 60 seconds of idling immediately before and immediately after the execution of a mode or schedule.

# ANALYSIS OF MHDT SCHEDULE

Each mode of the MHDT Schedule, as received from ARB, was analyzed to yield important parameters, such as maximum, minimum and average speed, standard deviation of speed, maximum acceleration and deceleration, percent idle, mass-specific energy (simply as the square of velocity) and standard deviation of mass-specific energy. Table 2 presents these values for the three modes. Values may be contrasted with values in Table 3, which presents analysis of the four HHDDT modes and the Heavy-Duty Urban Dynamometer Driving Schedule (UDDS), which appears in the Code of Federal Regulations and has been widely used to characterize diesel truck emissions [1, 6, 7, 8]. Table 3 also contains the data for the City-Suburban Heavy Vehicle Cycle (CSHVC) and the Highway Cycle, originally derived from activity of local delivery tractor-trailers [9, 10].

Table 2 Analysis parameters for the as-received Lower Speed Transient, Higher Speed Transient and Cruise modes of the MHDT schedule.

|  | Lower Speed Transient | Higher Speed Transient | Cruise |
| --- | --- | --- | --- |
| Maximum Speed (mph) | 28.9 | 58.2 | 66.0 |
| Minimum Speed (mph) | 0.0 | 0.0 | 0.0 |
| Average Speed (mph) | 11.1 | 22.1 | 41.2 |
| Standard Deviation of Speed (mph) | 10.7 | 18.0 | 26.0 |
| Maximum Acceleration (mph/s) | 5.00 | 5.52 | 4.60 |
| Maximum Deceleration (mph/s) | 5.52 | 5.40 | 4.81 |
| Percent Idle (%) | 23.3 | 15.3 | 5.5 |
| Average of Mass-specific Energy (mph2) | 237 | 810 | 2367 |
| Standard Deviation of Mass-specific Energy (mph2) | 296 | 919 | 1744 |

The UDDS was created using Monte-Carlo simulation. The three active (i.e., excluding the idle mode) HHDDT modes were derived from actual truck microtrips representing on-road activity, but were smoothed with a three second average before seeing general application.  The smoothed versions [5] were used to prepare the data shown in Table 3.  The CSHVC and Highway Cycle were both altered during their creation to remove excessive deceleration behavior before they saw general application, and the data in Table 3 reflect the altered cycle characteristics. Table 2 shows that the maximum deceleration rates in the new MHDT Lower Speed Transient, Higher Speed Transient and Cruise modes are larger than the cycles to which they are compared. Maximum acceleration rates are also high, and trucks with low power to test weight ratios may not be able to follow the trace during acceleration. However, the MHDT schedule will most often be applied to trucks that are lighter than those on which the comparative schedules in Table 3 are employed.

Table 3 Analysis parameters for four HHDDT, CSHVC and Highway mode.

|  | Transient | Cruise | Creep | UDDS | CSHVC | Highway |
| --- | --- | --- | --- | --- | --- | --- |
| Maximum Speed (mph) | 47.5 | 59.3 | 8.2 | 58.0 | 43.8 | 60.7 |
| Minimum Speed (mph) | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |
| Average Speed (mph) | 14.9 | 39.9 | 1.6 | 18.9 | 14.2 | 34.0 |
| Standard Deviation of Speed (mph) | 13.4 | 22.0 | 2.0 | 19.8 | 13.1 | 21.8 |
| Maximum Acceleration (mph/s) | 3.00 | 2.40 | 2.30 | 4.38 | 2.56 | 1.80 |
| Maximum Deceleration (mph/s) | 2.90 | 2.50 | 2.50 | 4.63 | 3.96 | 2.00 |
| Percent Idle (%) | 18.1 | 7.8 | 12.7 | 33.2 | 23.3 | 10.7 |
| Average of Mass-specific Energy (mph2) | 403 | 207 | 6.8 | 748 | 370 | 1629 |
| Standard Deviation of Mass-specific Energy (mph2) | 550 | 1320 | 45.7 | 1047 | 449 | 1338 |

The MHDT range encompasses trucks with a GVW rating varying by a factor of nearly 2.5, and the range of possible test weights will be even larger. Engine power will vary far less. At this time of writing, many light heavy-duty diesel pickup trucks are sporting over 300hp, while most Class 6 (19,001 to 26,000lb.,) trucks are likely to have engines of 180 to 250hp, and few Class 7 trucks will exceed 300hp.  In this way, power to weight ratios will vary widely for MHDT. Any single test schedule employing a speed-time target for MHDT must therefore reach a compromise for all the vehicles in the spectrum.

In executing a test for the Lower Speed Transient and the Cruise modes, idle time was added at the beginning of the modes. Also, idle time was added at the end of the Higher Speed Transient mode. It is traditional to start and stop emissions tests with a period of idle to synchronize vehicle operation and analyzer data acquisition. The original ARB MHDT Lower Speed Transient mode contained 1 second of idle at the beginning and 4 seconds of idle at the end. Thirty seconds of idle was added at the beginning of the target trace and 24 seconds of idle at the end of the target trace. The original ARB MHDT Higher Speed Transient mode contained 47 seconds of idle at the beginning and 5 seconds of idle at the end. Twenty-seven seconds of idle operations were added to the end of the target trace but the researchers did not alter the beginning of the trace. The original ARB MHDT Cruise mode contained 5 seconds of idle at the beginning and 5 seconds of idle at the end. Thirty seconds of idle was added at the beginning and 25 seconds at the end of the target trace. Details of idle addition are given in Appendix A.

# PROCUREMENT OF TEST VEHICLES

The new schedule was evaluated using MHDT. It was assumed that future MHDT testing would be conducted on trucks from 14,001 to 33,000lb. GVW, and that they may be tested at “laden” and “unladen” weights. A fully loaded 33,000lb. truck by definition must weigh 33,000lb., while an unladed (curb weight) 14,000lb. GVW truck may weigh as little as 8,000lb. It was not possible in this study to select a single vehicle to cover a range of 8,000 to 33,000lb., and so the investigators sought a truck in the 19,000 to 26,000lb. GVW range, with the intent of conducting testing at both laden and unladen weights on this vehicle.

Table 4 Vehicle information of the MHDT with manual transmission

| Vehicle Type | Delivery Flatbed Truck |
| --- | --- |
| Vehicle Manufacturer | GMC |
| Vehicle Model Year | 2000 |
| Gross Vehicle Weight (GVW) | 19500lb., 8833kg |
| Vehicle Tested Weight | 17550lb.,7950kg (laden), 9750lb., 4417kg (unladen) |
| Odometer Reading | 25999mile, 41832km |
| Transmission Type | Synchronized Manual |
| Transmission Configuration | 6 speed |
| Number of Axles | 2 |
| Engine Type | Isuzu 8.2L |
| Engine Displacement | 8.2liter |
| Number of Cylinders | 6 |
| Engine Rated Power | 200hp, 149kw |

Table 5 Vehicle information of the MHDT with automatic transmission

| Vehicle Type | Delivery Truck |
| --- | --- |
| Vehicle Manufacturer | Freightliner |
| Vehicle Model Year | 1999 |
| Gross Vehicle Weight (GVW) | 26000lb., 11778kg |
| Vehicle Tested Weight | 13000lb., 5889kg (one weight only) |
| Odometer Reading | 143619mile, 231083km |
| Transmission Type | Automatic |
| Number of Axles | 2 |
| Engine Type | Caterpillar 3126 |
| Engine Displacement | 7.2liter |
| Number of Cylinders | 6 |
| Engine Rated Power | 246hp, 183kw |

Figure 4 GMC truck with 6 speed manual transmission.

Figure 5 Freightliner truck with automatic transmission.

Contractually the investigators were bound to perform the MHDT schedule evaluation using only one MHDT.  However, the investigators considered the possible effects of transmission type on vehicle performance, and determined that the bulk of the testing should be performed with a truck with a manual transmission, but that a small number of test runs using a MHDT with an automatic transmission would also be informative.  Two trucks were therefore procured. Table 4 provides details of the MHDT with the manual transmission, and Table 5 provides details of the MHDT with the automatic transmission. Figure 4 and Figure 5 show photographs of the two trucks. For test purposes, the investigators chose to use 90% of GVW as the “laden” weight and 50% of GVW as the “unladen” weight, and the automatic truck was tested only at unladen weight.

# TEST APPARATUS

In executing the required testing, the researchers employed the WVU medium-duty chassis dynamometer, located in Riverside, CA at the time of testing. This dynamometer consisted of four, linked 19.75 inch diameter rolls on which the vehicle rear axle was positioned.  The rolls were connected via belt drives to a flywheel set and an eddy current power absorber. Various flywheels could be engaged to mimic a desired vehicle inertia weight. See Figure 6. Road load drag on the vehicle was mimicked partially by the irreversible (frictional) losses in the laboratory, and was adjusted to the correct value at each speed using the eddy current power absorber with closed-loop torque control.  The vehicle exhaust was ducted to the intake of a full-scale dilution tunnel, operating at a nominal flow rate of 1500scfm.  Dilution air was HEPA filtered. Table 6 presents the analyzers used for regulated gases and carbon dioxide concentration measurement. Two NOX analyzers were available, and both were employed to assist in data quality control and because NOX is a species of major interest from diesel vehicles. Particulate matter was determined using 70mm Pallflex T60A20 filters. Filters were conditioned in an environmental chamber before weighing.

Table 6 Analyzer used for regulated gases and carbon dioxide

| Gases | Analyzers |
| --- | --- |
| CO2 | (1)HORIBA AIA-210 NDIR; (2) California Analytical Model 300 NDIR |
| HC | Rosemount 402 Heated Flame Ionization Detection (HFID) |
| NOX | Rosemount 955 Chemiluminescent (Two identical units used) |
| CO | HORIBA AIA-210 NDIR |

For each run, bags of background (dilution) air were gathered, analyzed and used to correct gaseous emissions. Dilute gas bags were also collected during a run, but continuous data, integrated over the run, were preferred for reporting purposes. Separate runs were used to gather background PM levels for PM filter weight correction. Even though the tunnel had HEPA filtered air, PM backgrounds were essential because the tunnel itself might shed PM particles or outgas heavy hydrocarbons that would condense onto the PM.

# PRELIMINARY TEST RUNS

A “sequence number,” which represents a sequence of runs, and a run number within that sequence number denote each test run in this study.  For example, 6081-5 denotes run number 5 within sequence number 6081.

The researchers conducted preliminary runs using the standard transmission vehicle at laden weight (17,550lb.). WVU added idle time at the beginning and at the end of the target trace to facilitate data gathering. Appendix A describes the final version of three modes in detail. Table 7 shows the data gained from the preliminary runs in sequence number 6077. These preliminary runs revealed that some portions of the traces of the modes were difficult for the driver to follow.  Figure 7, Figure 8 and Figure 9 show the target speed versus time and actual speed versus time for the Lower Speed Transient,

Figure 6 Photograph of a portion of the medium-duty chassis dynamometer. The flywheel set is on the left, the power absorber is right of center, and two of the rollers are seen on the extreme right.

Higher Speed Transient and Cruise modes on the driver’s attempt at each mode. Figure 10, Figure 11 and Figure 12 present parity plots of actual speed at each second of the trace against target speed at each second of the trace for the same three runs. Specifically, (i) the target traces contained some speed dithering which the driver could not faithfully reproduce, (ii) some of the accelerations were too severe for the truck to follow, and (iii) some of the braking was at a high enough rate to cause tire slippage on the rolls, and the jumping of a drive belt on the dynamometer. The WVU researchers recommended to ARB that some deceleration and acceleration rates might be lessened, and that a three point smoothing process should be used to reduce speed dithering. ARB elected not to effect such changes, and the test program proceeded with the traces unaltered. The driver was instructed in subsequent runs to follow the trace as closely as possible, while avoiding excessive tire slippage or an unusually aggressive driving style.

Table 7 Data from preliminary runs on the standard transmission GMC vehicle at laden weight. Units are g/mile

| Run Seq. No. | Test Date | Mode | CO | NOX | NOX | HC | PM | CO2 | Miles |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 6077-1 | 2/6/03 | MHDTLO * | 2.82 | 8.7 | 8.4 | 0.56 | 0.26 | 1292 | 0.93 |
| 6077-2 | 2/6/03 | MHDTHI * | 1.55 | 6.2 | 6.1 | 0.34 | 0.20 | 1072 | 7.09 |
| 6077-3 | 2/6/03 | MHDTCR * | 0.84 | 4.3 | 4.2 | 0.20 | 0.09 | 639 | 21.29 |

*MHDTLO is Lower Speed Transient mode. MHDTHI is Higher Speed Transient mode. MHDTCR is Cruise mode.

Figure 7 Target speed and actual speed versus time for the Lower Speed Transient mode (6077-1) using the standard transmission vehicle at laden weight.

Figure 8 Target speed and actual speed versus time for the Higher Speed Transient mode (6077-2) using the standard transmission vehicle at laden weight.

Figure 9 Target speed and actual speed versus time for the Cruise mode (6077-3) using the standard transmission vehicle at laden weight.

Figure 10 Actual speed versus target speed for the Lower Speed Transient mode (6077-1) using the standard transmission vehicle at laden weight.

Figure 11 Actual speed versus target speed for the Higher Speed Transient mode (6077-2) using the standard transmission vehicle at laden weight. The string of points highest above the parity line represents a failure to brake as quickly as the target trace commands.

Figure 12 Actual speed versus target speed for the Cruise mode (6077-3) using the standard transmission vehicle at laden weight. Most points below the parity line correspond to the vehicle lagging an acceleration ramp.

# EMISSIONS DATA – STANDARD TRANSMISSION VEHICLE

The standard transmission GMC truck was exercised through several repeats of a sequence of modes in the order Lower Speed Transient, Higher Speed Transient and Cruise. These data were gathered under WVU test sequence numbers 6076, 6077, 6078 and 6081. In each sequence, run 1 is the Lower Speed Transient, run 2 is the Higher Speed Transient and run 3 is the Cruise mode.  In addition, sequence number 6081 ended with run 4 (a Higher Speed Transient) and run 5 (a Lower Speed Transient). These runs, 4 and 5 of sequence number 6081, were intended to determine whether the order in which modes occurred affected emissions.

Table 8 Emissions data on laden test runs for the sequence numbers 6076, 6077, 6078 and 6081. Where there are only two runs, statistics show the difference and difference/average values. Absent PM values are due to a filter weighing error detected during data processing.

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower Speed Transient | 6076-1 | 2.78 | 8.60 | 0.52 | 1238 | 0.260 |
|  | 6077-1 | 2.82 | 8.70 | 0.56 | 1292 | 0.257 |
|  | 6078-1 | 2.69 | 7.90 | 0.50 | 1257 |  |
|  | 6081-1 | 2.71 | 8.40 | 0.54 | 1244 |  |
|  | 6081-5 | 2.32 | 8.65 | 0.46 | 1305 |  |
|  | Ave. | 2.66 | 8.45 | 0.52 | 1267 | 0.26 |
|  | Std. Dev. | 0.20 | 0.33 | 0.04 | 30 | 0.00 |
|  | CV% | 7.5 | 3.9 | 7.3 | 2.3 | 1.1 |
| Higher Speed Transient | 6076-2 | 1.74 | 6.60 | 0.35 | 1053 | 0.222 |
|  | 6077-2 | 1.55 | 6.20 | 0.34 | 1072 | 0.195 |
|  | 6078-2 | 1.61 | 6.20 | 0.35 | 1041 |  |
|  | 6081-2 | 1.60 | 6.30 | 0.33 | 1016 |  |
|  | 6081-4 | 1.47 | 6.16 | 0.29 | 986 |  |
|  | Ave. | 1.59 | 6.29 | 0.33 | 1034 | 0.21 |
|  | Std. Dev. | 0.10 | 0.18 | 0.02 | 34 | 0.03 |
|  | CV% | 6.1 | 2.9 | 7.5 | 3.2 | 12.6 |
| Cruise | 6076-3 | 0.86 | 4.50 | 0.20 | 652 | 0.093 |
|  | 6077-3 | 0.84 | 4.30 | 0.20 | 639 | 0.085 |
|  | 6078-3 | 0.87 | 4.20 | 0.18 | 617 |  |
|  | 6081-3 | 0.85 | 4.50 | 0.17 | 620 |  |
|  | Ave. | 0.86 | 4.38 | 0.19 | 632 | 0.09 |
|  | Std. Dev. | 0.01 | 0.15 | 0.01 | 17 | 0.01 |
|  | CV% | 1.5 | 3.4 | 8.0 | 2.6 | 8.1 |

Table 8 shows the data for sequence numbers 6076, 6077, 6078 and 6081, with the data gathered by mode.  In this table, data are given in the most customary units of g/mile. Data for NOX show little variation from run to run of each mode, and it was also found that the two NOX analyzers in use agreed well. The NOX data also suggest that the order of modes does not matter in its influence on the Lower and Higher Speed Transient modes. Run 6081-5 (a Lower Speed Transient which followed a Higher Speed Transient) was similar to the other Lower Speed Transients.  Run 6081-4 (a Higher Speed Transient that followed a Cruise mode) was similar to the other Higher Speed Transients. Carbon monoxide (CO) data are often more variable from run to run than NOX data for diesel vehicles. This was the case in the present study for the Lower and Higher Speed Transient modes.  However, the CO values dropped steadily with time and this may be associated with the drivers’ increasing familiarity with the vehicle-schedule combination. Nevertheless, CO variations were modest and did not suggest a strong influence of order of modes on the results. Moreover, if CO values are examined in units of g/gallon, which tend to account for fuel economy changes due to driving style, the variations for the Higher Speed Transient are reduced further. Hydrocarbon data were consistently low, as one would expect for a modern diesel engine, and variation from run to run was acceptable. Values for HC also showed a trend of declining with time, which may correspond to increasing driver comfort with the task. It was noted that for the out-of-order runs (6081-4 and 6081-5), HC was lower than for other runs, so that there may be a small influence of prior run on HC. All CO2 coefficients of variance were below 4% for the runs, indicating a high level of repeatability of fuel consumption. In chassis dynamometer testing, CO2 variability arises not only from variability in gas and flow measurement, but also due to driver effects between test runs. It is therefore expected that variations would be larger than those typical in a diesel transient test cell.

Cumulative distance traveled was very repeatable for the Higher Speed Transient and Cruise modes. There was more variability for the Lower Speed Transient, with distances varying from 0.906 miles to 0.954 miles over five runs.  This variation is similar to the variation from run to run found in previous work on the HHDDT Creep mode, which also has a low average speed [5]. However, the Lower Speed Transient was still sufficiently repeatable not to raise concern about its application in inventory work. PM was not reported for sequence numbers 6078 and 6081 due to a weighing error that could not be corrected.

The investigators were concerned over PM data for sequence numbers 6078 and 6081. A block of PM filter weights, for both primary and secondary filters, appeared to have a scale zero offset of about 0.5 milligrams. Concern over this weighing offset obliged the researchers to conduct an additional set of runs, the results from which are discussed below, and PM data from the affected runs are not given in Table 8, and are not given in the Appendix B. Attempts to correct for this 0.5 milligram offset were not scientifically defensible.

Table 9 Emissions data for laden test runs for the sequence numbers 6104 and 6105.

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower Speed Transient | 6104-1 | 3.01 | 8.60 | 0.47 | 1276 | 0.279 |
|  | 6105-1 | 2.97 | 8.90 | 0.48 | 1329 | 0.298 |
|  | Ave. | 2.99 | 8.75 | 0.48 | 1303 | 0.29 |
|  | Std. Dev. | 0.04 | 0.30 | 0.01 | 53 | 0.02 |
|  | CV% | 1.3 | 3.4 | 2.1 | 4.1 | 6.6 |
| Higher Speed Transient | 6104-2 | 1.50 | 6.00 | 0.24 | 969 | 0.197 |
|  | 6105-2 | 1.44 | 6.00 | 0.25 | 965 | 0.182 |
|  | Ave. | 1.47 | 6.00 | 0.25 | 967 | 0.19 |
|  | Std. Dev. | 0.06 | 0.00 | 0.01 | 4 | 0.02 |
|  | CV% | 4.1 | 0.0 | 4.1 | 0.4 | 7.9 |
| Cruise | 6104-3 | 0.78 | 4.30 | 0.18 | 624 | 0.096 |
|  | 6105-3 | 0.78 | 4.40 | 0.19 | 629 | 0.097 |
|  | Ave. | 0.78 | 4.35 | 0.19 | 627 | 0.10 |
|  | Std. Dev. | 0.00 | 0.10 | 0.01 | 5 | 0.00 |
|  | CV% | 0.0 | 2.3 | 5.4 | 0.8 | 0.5 |

Re-runs of the laden schedule are associated with sequence numbers 6104 and 6105. These extra runs were conducted to compensate for the loss of PM data due to filter weighing concerns in sequence numbers 6078 and 6081. Data for sequence numbers 6104 and 6105 are given in Table 9. For the Lower Speed Transient, sequence numbers 6104 and 6105 produced NOX levels that agreed well between analyzers, agreed well between the two runs, and agreed well with the earlier data from sequence numbers 6076, 6077, 6078, and 6081. All these NOX data may be compared directly by consulting Appendix B. For the Lower Speed Transient, both CO and HC values agreed well for sequence numbers 6104 and 6105, and agreement with the prior runs in sequence numbers 6076, 6077 and 6078 was acceptable. PM values agreed very well between the re-runs in sequence numbers 6104 and 6105 and the original runs in sequence numbers 6076 and 6077. The PM data for sequence numbers 6078 and 6081 were known to be in error, and were excluded.

For the case of the Higher Speed Transient and the Cruise modes there was also good agreement between the re-runs (6104 and 6105) and prior runs (6076, 6077, 6078 and 6081) for NOX, with the greatest differences being on the order of 10%. Carbon monoxide values were also acceptably repeatable. Hydrocarbon values on the Lower Speed Transient and Higher Speed Transient modes were lower for sequence numbers 6104 and 6105 than for the earlier runs, but the HC values were all low and the difference was not deemed substantial. PM values were slightly higher for the re-runs on the Lower Speed Transient and Cruise but slightly lower for the Higher Speed Transient mode.

An overall conclusion is that sequence numbers 6076, 6077, 6078, 6081, 6104 and 6105 have shown that the three modes of the MHDT schedule are sufficiently repeatable to justify the use of the schedule in future research efforts.

Table 10 Emissions data from the GMC truck on laden test runs for the sequence numbers 6082, 6083 and 6084.

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower speed Transient | 6082-1 | 2.59 | 9.30 | 0.56 | 1392 | 0.245 |
|  | 6082-2 | 2.71 | 9.30 | 0.54 | 1291 | 0.247 |
|  | 6082-3 | 3.03 | 9.10 | 0.58 | 1427 | 0.267 |
|  | Ave. | 2.78 | 9.23 | 0.56 | 1370 | 0.25 |
|  | Std. Dev. | 0.23 | 0.12 | 0.02 | 71 | 0.01 |
|  | CV% | 8.2 | 1.3 | 3.6 | 5.2 | 4.8 |
| Higher Speed Transient | 6083-1 | 1.67 | 6.70 | 0.31 | 1044 | 0.249 |
|  | 6083-2 | 1.85 | 6.90 | 0.37 | 1126 | 0.198 |
|  | 6083-3 | 1.67 | 6.90 | 0.32 | 1090 | 0.180 |
|  | Ave. | 1.73 | 6.83 | 0.33 | 1087 | 0.21 |
|  | Std. Dev. | 0.10 | 0.12 | 0.03 | 41 | 0.04 |
|  | CV% | 6.0 | 1.7 | 9.6 | 3.8 | 17.3 |
| Cruise | 6084-1 | 0.83 | 5.20 | 0.18 | 656 | 0.090 |
|  | 6084-2 | 0.82 | 5.10 | 0.19 | 651 | 0.086 |
|  | 6084-3 | 0.82 | 4.90 | 0.18 | 659 | 0.086 |
|  | Ave. | 0.82 | 5.07 | 0.18 | 655 | 0.09 |
|  | Std. Dev. | 0.01 | 0.15 | 0.01 | 4 | 0.00 |
|  | CV% | 0.7 | 3.0 | 3.2 | 0.6 | 2.5 |

Laden runs were also conducted repeating three of the same modes in a row. Sequence number 6082 had three Lower Speed Transient runs in a row, 6083 had three Higher Speed Transients in a row, and 6084 has three Cruise modes in a row. Data, shown in Table 10 were very repeatable, even in the case of PM, which is difficult to quantify at low filter loadings. For the Lower Speed Transient, CO2 coefficient of variance was over 5%, but this may be expected at times for a low speed test with transient activity. It is possible that intermittent auxiliary loads on the engine might affect emissions slightly in the case of such low energy cycles [5].

One may also conclude that it is reasonable to execute repeat runs of the same mode directly after one another, since the order of runs showed no discernable influence on the resulting emissions.

Table 11 Emissions data on unladen test runs for the sequence numbers 6098, 6099, 6100 and 6101. Units are g/mile. Data are shown from only the primary NOX analyzer.

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower speed Transient | 6098-1 | 2.83 | 7.99 | 0.54 | 1144 | 0.229 |
|  | 6099-1 | 2.44 | 7.64 | 0.53 | 1067 | 0.179 |
|  | 6100-1 | 2.93 | 8.21 | 0.52 | 1167 | 0.260 |
|  | 6101-1 | 2.97 | 7.67 | 0.51 | 1088 | 0.174 |
|  | Average | 2.79 | 7.88 | 0.53 | 1116 | 0.21 |
|  | Std Dev | 0.24 | 0.27 | 0.01 | 47 | 0.04 |
|  | CV% | 8.6 | 3.5 | 2.5 | 4.2 | 19.6 |
| Higher Speed Transient | 6098-2 | 1.64 | 5.82 | 0.33 | 862 | 0.192 |
|  | 6099-2 | 1.46 | 5.57 | 0.30 | 809 | 0.148 |
|  | 6100-2 | 1.61 | 5.35 | 0.26 | 789 | 0.138 |
|  | 6101-2 | 1.56 | 5.24 | 0.28 | 785 | 0.140 |
|  | Average | 1.56 | 5.49 | 0.29 | 811 | 0.15 |
|  | Std Dev | 0.08 | 0.26 | 0.03 | 36 | 0.03 |
|  | CV% | 5.0 | 4.7 | 10.1 | 4.4 | 16.5 |
| Cruise | 6098-3 | 0.81 | 4.56 | 0.19 | 597 | 0.100 |
|  | 6099-3 | 0.87 | 4.44 | 0.19 | 582 | 0.094 |
|  | 6100-3 | 0.97 | 4.47 | 0.19 | 614 | 0.084 |
|  | 6101-3 | 0.94 | 4.27 | 0.19 | 599 | 0.091 |
|  | Average | 0.90 | 4.44 | 0.19 | 598 | 0.09 |
|  | Std Dev | 0.07 | 0.12 | 0.00 | 13 | 0.01 |
|  | CV% | 8.1 | 2.7 | 1.7 | 2.2 | 7.3 |

Unladen runs of the schedule appear in sequence numbers 6098, 6099, 6100 and 6101. The data are presented in Table 11. NOX and CO2 data are very repeatable. Particulate matter data were variable. PM and CO both arise from incomplete combustion and may be associated with engine transient effects. A previous study has shown that driving style could influence CO and PM emissions [11], although the recent evaluation study for the HHDDT schedule [5] found that driver influences were low or absent. Carbon dioxide data were more variable for the unladen Cruise mode than the laden Cruise mode. It may be that in the laden case, emissions are dominated more by the accelerations, which are repeatable in their energy demand, and hence cause greater run-to-run CO2 repeatability.

It is interesting to note that raising the test weight from unladen (50% GVW) to laden (90% GVW), which is an 80% increase in weight, caused fuel consumption to rise by approximately 19%. Table 12 shows fuel consumption increase and NOX increase from unladen (50% GVW) to laden (90% GVW) test runs for the Lower Speed Transient mode, Higher Speed Transient mode and Cruise mode of the MHDT schedule. WVU researchers have observed (and developed a “rule of thumb”) that an X% increase in test weight often gives roughly a (X/2)% increase in CO2 and NOX for HHDDT. The MHDT GMC vehicle showed a lower increase than this “rule of thumb” would suggest, perhaps because driveline losses, auxiliary loads and wind drag represent a higher proportion of total energy consumed than for the case of HHDDT.  For HHDDT inertial effects and tire losses dominate the energy use except for very high-speed test schedules.

Table 12 Fuel consumption and NOX increase from unladen (50% GVW) to laden (90% GVW) test runs for the three modes with the GMC vehicle.

| Test mode | Fuel consumption increase | NOX increase |
| --- | --- | --- |
| Lower Speed Transient | 19% | 14% |
| Higher Speed Transient | 30% | 18% |
| Cruise | 8% | 7% |

Continuous NOX data are presented in this report to demonstrate the difference between laden and unladen operation. Figure 13 shows a plot of NOX versus time for unladen run 6101-1 and laden run 6105-1 for the case of the Lower Speed Transient mode. Figure 14 shows a plot of NOX versus time for unladen run 6101-2 and laden run 6105-2 for the case of the Higher Speed Transient mode. Figure 15 shows a plot of NOX versus time for unladen run 6101-3 and laden run 6105-3 for the case of the Cruise mode.

Figure 13 NOX versus time for unladen run and laden run on the Lower Speed Transient mode.

Figure 14 NOX versus time for unladen run and laden run on the Higher Speed Transient mode.

Figure 15 NOX versus time for unladen run and laden run on the Cruise mode.

Figure 16 CO versus time for unladen run and laden run on the Higher Speed Transient mode.

Figure 17 HC versus time for unladen run and laden run on the Higher Speed Transient mode.

Continuous data for CO and HC during laden and unladen runs are presented for the Higher Speed Transient alone, and are shown in Figure 16 and Figure 17. In Figure 16, neither laden nor unladen runs are higher in value over the whole test mode, emphasizing that driver effects and run-to-run variations are evident with CO emissions. The cycle-averaged HC and CO values (in g/mile) differ little between laden and unladen runs, echoing the comparisons in Figure 16 and Figure 17.

# EMISSIONS DATA – AUTOMATIC TRANSMISSION VEHICLE

The automatic truck was tested at only one weight, namely 13,000lb., and each mode was run as a separate sequence number of three runs.

Table 13 Emissions data from the automatic Freightliner truck.

| Test Mode | Test Seq. No. | CO | NOX | HC | CO2 | PM |
| --- | --- | --- | --- | --- | --- | --- |
| Lower Speed Transient | 6108-3 | 3.57 | 16.62 | 0.50 | 1648 | 0.334 |
|  | 6108-4 | 3.45 | 16.28 | 0.48 | 1657 | 0.345 |
|  | 6108-5 | 3.62 | 16.28 | 0.48 | 1682 | 0.320 |
|  | Average | 3.55 | 16.39 | 0.49 | 1662 | 0.33 |
|  | Std Dev | 0.09 | 0.19 | 0.01 | 18 | 0.01 |
|  | CV% | 2.5 | 1.2 | 2.8 | 1.1 | 3.6 |
| Higher Speed Transient | 6109-1 | 1.89 | 12.85 | 0.35 | 1238 | 0.256 |
|  | 6109-2 | 1.91 | 12.50 | 0.35 | 1220 | 0.249 |
|  | 6109-3 | 1.98 | 12.43 | 0.33 | 1207 | 0.234 |
|  | Average | 1.93 | 12.59 | 0.35 | 1222 | 0.25 |
|  | Std Dev | 0.05 | 0.22 | 0.01 | 16 | 0.01 |
|  | CV% | 2.6 | 1.8 | 3.6 | 1.3 | 4.6 |
| Cruise | 6112-1 | 1.20 | 8.25 | 0.35 | 1133 | 0.125 |
|  | 6112-2 | 1.15 | 7.67 | 0.34 | 1093 | 0.157 |
|  | 6112-3 | 1.23 | 7.86 | 0.32 | 1077 | 0.143 |
|  | Average | 1.19 | 7.9 | 0.34 | 1101 | 0.14 |
|  | Std Dev | 0.04 | 0.30 | 0.02 | 29 | 0.02 |
|  | CV% | 3.1 | 3.7 | 4.7 | 2.6 | 11.4 |
| Test_D (UDDS) | 6113-3 | 2.13 | 7.49 | 0.50 | 1268 | 0.199 |
|  | 6113-4 | 1.99 | 7.75 | 0.49 | 1244 | 0.199 |
|  | 6113-5 | 1.99 | 7.49 | 0.53 | 1270 | 0.171 |
|  | Average | 2.03 | 7.57 | 0.51 | 1260 | 0.19 |
|  | Std Dev | 0.08 | 0.15 | 0.02 | 14 | 0.02 |
|  | CV% | 3.9 | 2.0 | 3.5 | 1.2 | 8.6 |

All test data acquired from the automatic Freightliner truck are shown in Table 13. Three repeat sequences were performed, and all gaseous data were very repeatable. PM data were repeatable for the Higher Speed Transient mode but had a coefficient of variation of over 11% on the Cruise mode. Figure 18, Figure 19 and Figure 20 show continuous NOX for the two transient modes and a Cruise run on the automatic truck. Oxides of nitrogen data were higher on all three modes than for the laden truck with a standard transmission, but PM data were comparable in units of g/mile. Carbon dioxide data show that the automatic truck had higher fuel consumption than the laden truck with a standard transmission. This might be expected noting the losses in the torque converter, and may also go to explain the higher NOX values. The automatic truck also had a higher GVW (and presumably a larger drivetrain) which would increase fuel consumption.

Figure 18 NOX versus time for the Lower Speed Transient mode for the automatic truck (run 6108-4).

Figure 19 NOX versus time for the Higher Speed Transient mode for the automatic truck (run 6109-2).

Figure 20 NOX versus time for the Cruise mode for the automatic truck (run 6112-2).

# COMPARISION WITH DATA FROM THE UDDS (TEST_D)

During the course of the study, some runs were completed on the Heavy-Duty UDDS, also known as Test_D. The GMC truck with the standard transmission was exercised through laden and unladen UDDS runs in sequence numbers 6081 and 6100. The run in 6081 had no final PM data. Data are discussed here in units of g/mile. Laden operation produced NOX data of a similar level to the Higher Speed Transient mode of the MHDT schedule. Unladen operation produced NOX at a level for the UDDS that lay above the NOX data for the Cruise and Higher Speed Transient mode, but below the Lower Speed Transient mode data. For the automatic truck, three runs of the UDDS were performed, as shown in Table 13. The UDDS yielded lower NOX values than the Lower or Higher Speed Transient modes. UDDS NOX levels were slightly lower than Cruise mode values.

# CONCLUSIONS

A new MHDT schedule, consisting of three modes (Lower Speed Transient, Higher Speed Transient and Cruise modes) was created from trips representing real-world vehicle use. To examine the suitability of the schedule for MHDT emissions characterization, and the repeatability of emissions using the modes, data were acquired using a GMC truck with a standard transmission at laden (17,550lb, 90% GVW) and unladen (9,750lb, 50% GVW) test weights, and a Freightliner truck with an automatic transmission at a single test weight of 13,000lb (50% GVW). Emissions data for CO, HC, NOX, CO2 and PM were computed in units of g/cycle, g/mile, g/ahp-hr, g/minute (or g/s) and g/gallon, and data were examined and compared primarily in units of g/mile. The laden GMC truck with a manual transmission could not follow some acceleration and deceleration ramps precisely, but data for gases for all three modes proved acceptably repeatable. However, PM variations exceeded 10% in some circumstances, and may be due to driver variability.

The GMC truck was able to follow the trace more closely when unladen, and the Freightliner truck with an automatic transmission was able to follow closely when unladen. Both transmission type and power to test weight ratio influence the ability to follow the trace. Typical unladen emissions values for the GMC truck were 7.88g/mile NOX and 0.21g/mile PM (Lower Speed Transient), 5.49g/mile NOX and 0.15g/mile PM (Higher Speed Transient) and 4.44g/mile NOX and 0.092g/mile PM (Cruise). NOX rose by 14%, 18% and 7% on these three respective modes for laden operation. NOX data for the GMC truck for the laden UDDS were similar to those for the Higher Speed Transient mode. Emissions for the automatic transmission Freightliner vehicle were 16.39g/mile NOX and 0.33g/mile PM (Lower Speed Transient), 12.60g/mile NOX and 0.25g/mile PM (Higher Speed Transient) and 7.93g/mile NOX and 0.14g/mile PM (Cruise mode). The automatic transmission vehicle yielded less run-to-run variation in CO2 (and hence fuel consumed) than the manual transmission vehicle for the two transient modes (see Tables 10 and 13) suggesting that some variability can be ascribed to transmission type. The testing experience and data repeatability suggest that the new MHDT schedule is well suited to MHDT emissions characterization. It was also considered that testing using several runs of the same mode in a row does not compromise NOx and PM results, although some data suggested that the order of testing may change the measured HC value.

# REFERENCES

YANOWITZ, J., McCORMICK, R.L., GRABOSKI, M.S., “In-Use Emissions from Heavy-Duty Diesel Vehicles,” Environmental Science and Technology, Vol. 34, No. 5, pp 729-739, 2000.

CLARK, N.N., TEHRANIAN, A., NINE, R.D., and JARRETT, R., "Translation of Distance-Specific Emissions Rates between Different Chassis Test Cycles using Artificial Neural Networks," SAE Spring 2002 Fuels & Lubricants Meeting, Reno, NV, SAE Paper 2002-01-1754.

CLARK, N.N., GAUTAM, M., WAYNE, W.S., THOMPSON, G., NINE, R.D., RIDDLE, W., LYONS, D.W., and MALDONADO, H., "Regulated Emissions from the California Heavy Heavy-Duty Diesel Truck Fleet Determined in the E55 Emissions Inventory Program,” Coordinating Research Council 13th On-Road Emissions Workshop, San Diego, Ca., April 2003.

CLARK, N.N., GAUTAM, M., WAYNE, W.S., NINE, R.D., and MALDONADO, H., "Emissions Measurements from Repair and Retest of Class 8 Trucks in the E55 Emissions Inventory Study," Coordinating Research Council 13th On-Road Emissions Workshop, San Diego, Ca., April  2003.

GAUTAM, M., CLARK, N.N., RIDDLE, W., NINE, R., WAYNE, W.S., MALDONADO, H., AGRAWAL, A. and CARLOCK, M., “Development and Initial Use of a Heavy Duty Diesel Truck Test Schedule for Emissions Characterization,” SAE Spring 2002 Fuels & Lubricants Meeting, Reno, NV, SAE Paper 2002-01-1753.

NINE, R.D., CLARK, N.N., and NORTON, P. "Effects of Multiple Driving Test Schedules Performed on Two Heavy-Duty Vehicles," SAE Fuels & Lubricants Meeting, Baltimore, Oct. 2000, SAE Paper 2000-01-2818.

DIETZMANN, H.E. and WARNER-SELPH, M.A., “Comparison of Emissions from Heavy-Duty Engines and Vehicles during Transient Operation,” ASME Paper 85-DGP-10, Energy Sources and Technology Conference, Dallas, TX, 1985.

Code of Federal Regulations, Title 40, Paart86, Web Access: http://www.gpoaccess.gov/cfr/about.html.

NINE, R.D., CLARK, N.N., DALEY, J.J. and ATKINSON, C.M., "Development of a heavy-duty chassis dynamometer driving route," Proc. Inst. Mech. Engrs. Part D., Jour. of Automobile Eng., Vol. 213 pp. 561-574.

CLARK, N.N., DALEY, J.J., NINE, R.D. and ATKINSON, C.M., "Application of the new City-Suburban Heavy Vehicle Route (CSHVR) to Truck Emissions Characterization," SAE Fuels & Lubricants Meeting, Detroit, May 1999, SAE Paper 1999-01-1467.

CLARK, N.N., GAUTAM, M., RAPP, B.L., LYONS, D.W., GRABOSKI, M.S., McCORMICK, R.L., ALLEMAN, T.L. and NORTON, P., "Transit Bus Emissions Characterization by Two Chassis Dynamometer Laboratories: Results and Issues," 1999 SAE Transactions, Jour. of Fuels & Lubricants, Vol. 108, pp. 801-812.

# APPENDIX A: MHDT Schedule

MHDT Lower Speed Transient

The original ARB MHDT Lower Speed Transient mode contained 1 second of idle at the beginning and 4 seconds of idle at the end.

WVU added 30 seconds of idle at the beginning of the target trace and 24 seconds of idle at the end of the target trace.

Sample system startup event sequencing consume 20 seconds of the idle period at the beginning of the target trace prior to start of data leaving 9 seconds of idle between start of data and the first acceleration.

The net change in idle operation is +33 seconds.

MHDT Higher Speed Transient

The original ARB MHDT Higher Speed Transient mode contained 47 seconds of idle at the beginning and 5 seconds of idle at the end.

WVU added 27 seconds of idle operation to the end of the target trace but did not alter the beginning of the trace.

Sample system startup event sequencing consumes 20 seconds of the idle at the beginning of the cycle prior to the start of data logging resulting in 27 seconds of idle between the start of data and the first acceleration.

The total idle period between the last deceleration and the end of the test is 22 seconds.

The net change in idle operation is +2 seconds.

MHDT Cruise Cycle

The original ARB MHDT Cruise mode contained 5 seconds of idle at the beginning and 5 seconds of idle at the end.

WVU added 30 seconds of idle at the beginning and 25 seconds at the end of the target trace.

Data collection begins 20 seconds after the target trace appears on the driver’s monitor. The first 20 seconds of cycle pre-roll is consumed by sample system startup event sequencing and no data are recorded until 20 seconds into the target trace.

In the final execution of the MHDT Cruise mode, WVU added 5 seconds at the beginning for a total of 10 seconds of idle before the first acceleration.  WVU added 20 seconds of idle to the end of the cycle for a total idle period of 25 seconds from the end of the last deceleration to the end of the test. This allows the exhaust from the last microtrip to make its way through the dilution tunnel and sampling system.

The net change in total idle is +25 seconds.

# APPENDIX B: Emissions data from this evaluation program.

The average and standard deviation did not consider “bad” data in the following Appendix B table, B1 to B10.

### TABLE B1: Emissions data from GMC truck (units are g/cycle).

| E55CRC-(truck) | Test ID | Test Run ID | CO (g/cycle) | NOx1 (g/cycle) | NOx2 (g/cycle) | HC (g/cycle) | PM (g/cycle) | CO2 (g/cycle) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LADEN |
|  | 6076 | 1 | 2.6414 | 8.1738 | 7.8881 | 0.4887 | 0.2465 | 1174 |
| MHDTLO | 6077 | 1 | 2.6297 | 8.1426 | 7.8572 | 0.5193 | 0.2398 | 1206 |
| Bad PM | 6078 | 1 | 2.5666 | 7.5821 | 7.4185 | 0.4815 |  | 1200 |
| Bad PM | 6081 | 1 | 2.4597 | 7.6088 | 7.3038 | 0.4902 |  | 1127 |
| Bad PM | 6081 | 5 | 2.1571 | 8.0564 | 7.9086 | 0.4310 |  | 1215 |
|  | 6104 | 1 | 2.8702 | 8.2356 | 8.3618 | 0.4474 | 0.2665 | 1218 |
|  | 6105 | 1 | 2.8071 | 8.4126 | 8.4448 | 0.4532 | 0.2821 | 1258 |
|  |  | Average | 2.7371 | 8.2412 | 8.1380 | 0.4771 | 0.2587 | 1214 |
|  |  | Std Dev | 0.1201 | 0.1207 | 0.3085 | 0.0335 | 0.0193 | 34.63 |
|  |  | CV | 4.3895 | 1.4641 | 3.7909 | 7.0203 | 7.4606 | 2.85 |
| MHDTHI | 6076 | 2 | 12.3474 | 46.6217 | 45.5505 | 2.4865 | 1.5719 | 7467 |
|  | 6077 | 2 | 11.0057 | 43.8154 | 43.0644 | 2.4177 | 1.3849 | 7602 |
| Bad PM | 6078 | 2 | 11.3620 | 43.6226 | 42.5014 | 2.4359 |  | 7330 |
| Bad PM | 6081 | 2 | 11.2055 | 43.8559 | 42.9992 | 2.3012 |  | 7115 |
| Bad PM | 6081 | 4 | 10.4013 | 43.4435 | 42.3088 | 2.0381 |  | 6957 |
|  | 6104 | 2 | 10.9653 | 44.0866 | 44.9004 | 1.7423 | 1.4365 | 7071 |
|  | 6105 | 2 | 10.5160 | 43.4821 | 42.9204 | 1.8471 | 1.3235 | 7021 |
|  |  | Average | 11.2086 | 44.5015 | 44.1089 | 2.1234 | 1.4292 | 7290 |
|  |  | Std Dev | 0.7909 | 1.4350 | 1.3176 | 0.3830 | 0.1058 | 288.18 |
|  |  | CV | 7.0566 | 3.2245 | 2.9872 | 18.0373 | 7.4000 | 3.95 |
| MHDTCR | 6076 | 3 | 18.2946 | 95.2034 | 93.7417 | 4.2551 | 1.9619 | 13807 |
|  | 6077 | 3 | 17.9118 | 92.1961 | 90.4374 | 4.3618 | 1.8188 | 13596 |
| Bad PM | 6078 | 3 | 18.4217 | 89.7983 | 87.6085 | 3.8888 |  | 13077 |
| Bad PM | 6081 | 3 | 18.0010 | 94.2642 | 88.3867 | 3.6854 |  | 13130 |
|  | 6104 | 3 | 16.6973 | 92.4586 | 90.9127 | 3.8467 | 2.0461 | 13282 |
|  | 6105 | 3 | 16.6689 | 92.8345 | 90.2227 | 4.0654 | 2.0571 | 13394 |
|  |  | Average | 17.3932 | 93.1732 | 91.3286 | 4.1323 | 1.9710 | 13520 |
|  |  | Std Dev | 0.8347 | 1.3786 | 1.6343 | 0.2264 | 0.1100 | 231.59 |
|  |  | CV | 4.7992 | 1.4796 | 1.7895 | 5.4787 | 5.5810 | 1.71 |
| Test_D |  |  |  |  |  |  |  |  |
| Bad PM | 6081 | 6 | 8.5619 | 33.0847 | 32.1863 | 1.6490 |  | 4938 |
| MHDTLO | 6082 | 1 | 2.4417 | 8.7656 | 8.3120 | 0.5256 | 0.2306 | 1311 |
|  | 6082 | 2 | 2.6052 | 8.9497 | 8.7822 | 0.5172 | 0.2376 | 1239 |
|  | 6082 | 3 | 2.8644 | 8.6350 | 8.2655 | 0.5434 | 0.2526 | 1348 |
|  |  | Average | 2.6371 | 8.7835 | 8.4532 | 0.5287 | 0.2403 | 1299 |
|  |  | Std Dev | 0.2131 | 0.1581 | 0.2858 | 0.0134 | 0.0112 | 55.41 |
|  |  | CV | 8.0820 | 1.8001 | 3.3813 | 2.5294 | 4.6698 | 4.26 |
| E55CRC-(truck) | Test ID | Test Run ID | CO (g/cycle) | NOx1 (g/cycle) | NOx2 (g/cycle) | HC (g/cycle) | PM (g/cycle) | CO2 (g/cycle) |
| MHDTHI | 6083 | 1 | 11.9118 | 47.8166 | 46.2622 | 2.2438 | 1.7805 | 7455 |
|  | 6083 | 2 | 13.3387 | 49.9829 | 48.0816 | 2.6842 | 1.4290 | 8139 |
|  | 6083 | 3 | 11.9837 | 49.1025 | 47.1637 | 2.2909 | 1.2887 | 7809 |
|  |  | Average | 12.4114 | 48.9673 | 47.1692 | 2.4063 | 1.4994 | 7801 |
|  |  | Std Dev | 0.8038 | 1.0895 | 0.9097 | 0.2418 | 0.2533 | 342.29 |
|  |  | CV | 6.4767 | 2.2249 | 1.9286 | 10.0482 | 16.8949 | 4.39 |
| MHDTCR | 6084 | 1 | 17.5914 | 111.5511 | 107.0204 | 3.7395 | 1.9071 | 13944 |
|  | 6084 | 2 | 17.4360 | 109.1180 | 108.4595 | 3.9716 | 1.8335 | 13846 |
|  | 6084 | 3 | 17.4666 | 103.3805 | 99.7168 | 3.7805 | 1.8226 | 14000 |
|  |  | Average | 17.4980 | 108.0165 | 105.0655 | 3.8305 | 1.8544 | 13930 |
|  |  | Std Dev | 0.0823 | 4.1952 | 4.6877 | 0.1239 | 0.0459 | 77.63 |
|  |  | CV | 0.4704 | 3.8838 | 4.4617 | 3.2333 | 2.4777 | 0.56 |
| UNLADEN |
| MHDTLO | 6098 | 1 | 2.7420 | 7.7399 | 7.4596 | 0.5238 | 0.2215 | 1109 |
|  | 6099 | 1 | 2.3828 | 7.4571 | 7.2465 | 0.5210 | 0.1746 | 1041 |
|  | 6100 | 1 | 2.8615 | 8.0094 | 7.8823 | 0.5050 | 0.2537 | 1138 |
|  | 6101 | 1 | 2.8994 | 7.4955 | 7.0717 | 0.5002 | 0.1704 | 1063 |
|  |  | Average | 2.7214 | 7.6755 | 7.4150 | 0.5125 | 0.2051 | 1088 |
|  |  | Std Dev | 0.2355 | 0.2554 | 0.3496 | 0.0116 | 0.0399 | 43.74 |
|  |  | CV | 8.6534 | 3.3279 | 4.7144 | 2.2646 | 19.4353 | 4.02 |
| MHDTHI | 6098 | 2 | 11.9265 | 42.4176 | 42.1604 | 2.3972 | 1.3989 | 6285 |
|  | 6099 | 2 | 10.5676 | 40.3048 | 39.3710 | 2.1862 | 1.0724 | 5859 |
|  | 6100 | 2 | 11.5751 | 38.5564 | 37.5101 | 1.8737 | 0.9917 | 5690 |
|  | 6101 | 2 | 11.2164 | 37.7937 | 37.3375 | 2.0204 | 1.0090 | 5660 |
|  |  | Average | 11.3214 | 39.7681 | 39.0947 | 2.1194 | 1.1180 | 5874 |
|  |  | Std Dev | 0.5802 | 2.0554 | 2.2416 | 0.2249 | 0.1905 | 288.10 |
|  |  | CV | 5.1246 | 5.1685 | 5.7336 | 10.6130 | 17.0360 | 4.90 |
| MHDTCR | 6098 | 3 | 17.1172 | 97.0192 | 92.0016 | 4.0499 | 2.1203 | 12686 |
|  | 6099 | 3 | 18.5028 | 94.3183 | 91.3245 | 3.9392 | 2.0047 | 12372 |
|  | 6100 | 3 | 20.5502 | 95.1947 | 88.5587 | 4.0711 | 1.7840 | 13062 |
|  | 6101 | 3 | 20.1099 | 91.0831 | 88.4101 | 4.1010 | 1.9291 | 12773 |
|  |  | Average | 19.0700 | 94.4039 | 90.0737 | 4.0403 | 1.9595 | 12723 |
|  |  | Std Dev | 1.5713 | 2.4833 | 1.8569 | 0.0706 | 0.1410 | 284.01 |
|  |  | CV | 8.2398 | 2.6305 | 2.0615 | 1.7468 | 7.1963 | 2.23 |
| Test_D | 6100 | 4 | 11.0848 | 31.8928 | 32.5019 | 2.0254 | 0.7744 | 4520 |

### TABLE B2: Emissions data from GMC truck (units are g/mile).

| E55CRC-(truck) | Test ID | Test Run ID | CO (g/mile) | NOx1 (g/mile) | NOx2 (g/mile) | HC (g/mile) | PM (g/mile) | CO2 (g/mile) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LADEN |
| MHDTLO | 6076 | 1 | 2.7846 | 8.6171 | 8.3158 | 0.5152 | 0.2598 | 1238 |
|  | 6077 | 1 | 2.8183 | 8.7265 | 8.4206 | 0.5565 | 0.2570 | 1292 |
| Bad PM | 6078 | 1 | 2.6892 | 7.9440 | 7.7727 | 0.5044 |  | 1257 |
| Bad PM | 6081 | 1 | 2.7146 | 8.3975 | 8.0609 | 0.5411 |  | 1244 |
| Bad PM | 6081 | 5 | 2.3167 | 8.6525 | 8.4938 | 0.4629 |  | 1305 |
|  | 6104 | 1 | 3.0077 | 8.6303 | 8.7626 | 0.4688 | 0.2792 | 1276 |
|  | 6105 | 1 | 2.9674 | 8.8930 | 8.9270 | 0.4790 | 0.2983 | 1329 |
|  |  | Average | 2.8945 | 8.7167 | 8.6065 | 0.5049 | 0.2736 | 1284 |
|  |  | Std Dev | 0.1096 | 0.1272 | 0.2864 | 0.0397 | 0.0192 | 38.08 |
|  |  | CV | 3.7857 | 1.4595 | 3.3280 | 7.8694 | 7.0178 | 2.97 |
| MHDTHI | 6076 | 2 | 1.7410 | 6.5738 | 6.4227 | 0.3506 | 0.2216 | 1053 |
|  | 6077 | 2 | 1.5520 | 6.1786 | 6.0727 | 0.3409 | 0.1953 | 1072 |
| Bad PM | 6078 | 2 | 1.6144 | 6.1984 | 6.0391 | 0.3461 |  | 1041 |
| Bad PM | 6081 | 2 | 1.6003 | 6.2632 | 6.1409 | 0.3286 |  | 1016 |
| Bad PM | 6081 | 4 | 1.4740 | 6.1565 | 5.9957 | 0.2888 |  | 986 |
|  | 6104 | 2 | 1.5021 | 6.0394 | 6.1509 | 0.2387 | 0.1968 | 969 |
|  | 6105 | 2 | 1.4448 | 5.9740 | 5.8968 | 0.2538 | 0.1818 | 965 |
|  |  | Average | 1.5600 | 6.1915 | 6.1358 | 0.2960 | 0.1989 | 1015 |
|  |  | Std Dev | 0.1284 | 0.2688 | 0.2188 | 0.0579 | 0.0166 | 55.90 |
|  |  | CV | 8.2301 | 4.3413 | 3.5663 | 19.5739 | 8.3428 | 5.51 |
| MHDTCR | 6076 | 3 | 0.8637 | 4.4945 | 4.4255 | 0.2009 | 0.0926 | 652 |
|  | 6077 | 3 | 0.8414 | 4.3306 | 4.2480 | 0.2049 | 0.0854 | 639 |
| Bad PM | 6078 | 3 | 0.8687 | 4.2344 | 4.1312 | 0.1834 |  | 617 |
| Bad PM | 6081 | 3 | 0.8499 | 4.4506 | 4.1731 | 0.1740 |  | 620 |
|  | 6104 | 3 | 0.7840 | 4.3411 | 4.2685 | 0.1806 | 0.0961 | 624 |
|  | 6105 | 3 | 0.7827 | 4.3591 | 4.2365 | 0.1909 | 0.0966 | 629 |
|  |  | Average | 0.8179 | 4.3814 | 4.2946 | 0.1943 | 0.0927 | 636 |
|  |  | Std Dev | 0.0410 | 0.0764 | 0.0883 | 0.0109 | 0.0051 | 12.40 |
|  |  | CV | 5.0094 | 1.7430 | 2.0550 | 5.5925 | 5.5480 | 1.95 |
| Test_D |  |  |  |  |  |  |  |  |
| Bad PM | 6081 | 6 | 1.5457 | 5.9730 | 5.8108 | 0.2977 |  | 892 |
| MHDTLO | 6082 | 1 | 2.5941 | 9.3127 | 8.8307 | 0.5584 | 0.2450 | 1392 |
|  | 6082 | 2 | 2.7132 | 9.3208 | 9.1463 | 0.5386 | 0.2474 | 1291 |
|  | 6082 | 3 | 3.0315 | 9.1388 | 8.7478 | 0.5751 | 0.2673 | 1427 |
|  |  | Average | 2.7796 | 9.2574 | 8.9082 | 0.5574 | 0.2532 | 1370 |
|  |  | Std Dev | 0.2261 | 0.1028 | 0.2103 | 0.0183 | 0.0122 | 70.91 |
|  |  | CV | 8.1353 | 1.1103 | 2.3603 | 3.2744 | 4.8308 | 5.18 |
| MHDTHI | 6083 | 1 | 1.6685 | 6.6977 | 6.4800 | 0.3143 | 0.2494 | 1044 |
|  | 6083 | 2 | 1.8458 | 6.9165 | 6.6534 | 0.3714 | 0.1977 | 1126 |
|  | 6083 | 3 | 1.6734 | 6.8566 | 6.5859 | 0.3199 | 0.1800 | 1090 |
| E55CRC-(truck) | Test ID | Test Run ID | CO (g/mile) | NOx1 (g/mile) | NOx2 (g/mile) | HC (g/mile) | PM (g/mile) | CO2 (g/mile) |
|  |  | Average | 1.7292 | 6.8236 | 6.5731 | 0.3352 | 0.2090 | 1087 |
|  |  | Std Dev | 0.1010 | 0.1131 | 0.0874 | 0.0315 | 0.0361 | 41.16 |
|  |  | CV | 5.8393 | 1.6572 | 1.3301 | 9.3956 | 17.2553 | 3.79 |
| MHDTCR | 6084 | 1 | 0.8278 | 5.2492 | 5.0360 | 0.1760 | 0.0897 | 656 |
|  | 6084 | 2 | 0.8202 | 5.1333 | 5.1023 | 0.1868 | 0.0863 | 651 |
|  | 6084 | 3 | 0.8216 | 4.8630 | 4.6906 | 0.1778 | 0.0857 | 659 |
|  |  | Average | 0.8232 | 5.0818 | 4.9430 | 0.1802 | 0.0872 | 655 |
|  |  | Std Dev | 0.0040 | 0.1982 | 0.2210 | 0.0058 | 0.0022 | 3.65 |
|  |  | CV | 0.4877 | 3.8998 | 4.4716 | 3.2248 | 2.4965 | 0.56 |
| UNLADEN |
| MHDTLO | 6098 | 1 | 2.8293 | 7.9864 | 7.6971 | 0.5404 | 0.2286 | 1144 |
|  | 6099 | 1 | 2.4413 | 7.6403 | 7.4245 | 0.5338 | 0.1789 | 1067 |
|  | 6100 | 1 | 2.9332 | 8.2102 | 8.0799 | 0.5177 | 0.2601 | 1167 |
|  | 6101 | 1 | 2.9671 | 7.6706 | 7.2369 | 0.5119 | 0.1744 | 1088 |
|  |  | Average | 2.7927 | 7.8769 | 7.6096 | 0.5260 | 0.2105 | 1116 |
|  |  | Std Dev | 0.2415 | 0.2718 | 0.3661 | 0.0134 | 0.0412 | 46.73 |
|  |  | CV | 8.6471 | 3.4504 | 4.8105 | 2.5401 | 19.5615 | 4.19 |
| MHDTHI | 6098 | 2 | 1.6363 | 5.8197 | 5.7844 | 0.3289 | 0.1919 | 862 |
|  | 6099 | 2 | 1.4592 | 5.5655 | 5.4366 | 0.3019 | 0.1481 | 809 |
|  | 6100 | 2 | 1.6055 | 5.3478 | 5.2027 | 0.2599 | 0.1375 | 789 |
|  | 6101 | 2 | 1.5557 | 5.2419 | 5.1786 | 0.2802 | 0.1399 | 785 |
|  |  | Average | 1.5642 | 5.4937 | 5.4006 | 0.2927 | 0.1544 | 811 |
|  |  | Std Dev | 0.0775 | 0.2557 | 0.2811 | 0.0296 | 0.0254 | 35.54 |
|  |  | CV | 4.9517 | 4.6543 | 5.2052 | 10.1085 | 16.4786 | 4.38 |
| MHDTCR | 6098 | 3 | 0.8051 | 4.5633 | 4.3273 | 0.1905 | 0.0997 | 597 |
|  | 6099 | 3 | 0.8706 | 4.4377 | 4.2968 | 0.1853 | 0.0943 | 582 |
|  | 6100 | 3 | 0.9652 | 4.4713 | 4.1596 | 0.1912 | 0.0838 | 614 |
|  | 6101 | 3 | 0.9438 | 4.2748 | 4.1493 | 0.1925 | 0.0905 | 599 |
|  |  | Average | 0.8962 | 4.4368 | 4.2333 | 0.1899 | 0.0921 | 598 |
|  |  | Std Dev | 0.0730 | 0.1203 | 0.0920 | 0.0031 | 0.0067 | 12.87 |
|  |  | CV | 8.1455 | 2.7123 | 2.1722 | 1.6509 | 7.2743 | 2.15 |
| Test_D | 6100 | 4 | 1.9946 | 5.7389 | 5.8485 | 0.3645 | 0.1394 | 813 |

### TABLE B3: Emissions data from GMC truck (units are g/ahp-hr.)

| E55CRC-(truck) | Test ID | Test Run ID | CO g/ahp-hr | NOx1 g/ahp-hr | NOx2 g/ahp-hr | HC g/ahp-hr | PM g/ahp-hr | CO2 g/ahp-hr |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LADEN |
| MHDTLO | 6076 | 1 | 2.5332 | 7.8391 | 7.5651 | 0.4686 | 0.2364 | 1126 |
|  | 6077 | 1 | 2.4183 | 7.4881 | 7.2257 | 0.4775 | 0.2205 | 1109 |
| Bad PM | 6078 | 1 | 2.4097 | 7.1184 | 6.9648 | 0.4520 |  | 1126 |
| Bad PM | 6081 | 1 | 2.3581 | 7.2945 | 7.0021 | 0.4700 |  | 1081 |
| Bad PM | 6081 | 5 | 1.8434 | 6.8848 | 6.7585 | 0.3683 |  | 1038 |
|  | 6104 | 1 | 2.6222 | 7.5242 | 7.6395 | 0.4088 | 0.2434 | 1113 |
|  | 6105 | 1 | 2.5202 | 7.5527 | 7.5816 | 0.4068 | 0.2533 | 1129 |
|  |  | Average | 2.5235 | 7.6010 | 7.5030 | 0.4404 | 0.2384 | 1119 |
|  |  | Std Dev | 0.0835 | 0.1609 | 0.1876 | 0.0379 | 0.0138 | 9.82 |
|  |  | CV | 3.3084 | 2.1169 | 2.5001 | 8.5992 | 5.7905 | 0.88 |
| MHDTHI | 6076 | 2 | 1.6341 | 6.1701 | 6.0283 | 0.3291 | 0.2080 | 988 |
|  | 6077 | 2 | 1.3909 | 5.5375 | 5.4426 | 0.3056 | 0.1750 | 961 |
| Bad PM | 6078 | 2 | 1.5104 | 5.7990 | 5.6500 | 0.3238 |  | 974 |
| Bad PM | 6081 | 2 | 1.4747 | 5.7715 | 5.6587 | 0.3028 |  | 936 |
| Bad PM | 6081 | 4 | 1.3104 | 5.4733 | 5.3303 | 0.2568 |  | 876 |
|  | 6104 | 2 | 1.4583 | 5.8633 | 5.9716 | 0.2317 | 0.1910 | 940 |
|  | 6105 | 2 | 1.4120 | 5.8382 | 5.7628 | 0.2480 | 0.1777 | 943 |
|  |  | Average | 1.4738 | 5.8523 | 5.8013 | 0.2786 | 0.1880 | 958 |
|  |  | Std Dev | 0.1105 | 0.2585 | 0.2650 | 0.0462 | 0.0151 | 22.11 |
|  |  | CV | 7.4971 | 4.4167 | 4.5684 | 16.5905 | 8.0398 | 2.31 |
| MHDTCR | 6076 | 3 | 1.1865 | 6.1744 | 6.0796 | 0.2760 | 0.1272 | 895 |
|  | 6077 | 3 | 1.1930 | 6.1405 | 6.0233 | 0.2905 | 0.1211 | 906 |
| Bad PM | 6078 | 3 | 1.2250 | 5.9711 | 5.8255 | 0.2586 |  | 870 |
| Bad PM | 6081 | 3 | 1.1774 | 6.1657 | 5.7812 | 0.2411 |  | 859 |
|  | 6104 | 3 | 1.2313 | 6.8179 | 6.7039 | 0.2837 | 0.1509 | 979 |
|  | 6105 | 3 | 1.2653 | 7.0468 | 6.8486 | 0.3086 | 0.1562 | 1017 |
|  |  | Average | 1.2190 | 6.5449 | 6.4139 | 0.2897 | 0.1389 | 949 |
|  |  | Std Dev | 0.0366 | 0.4573 | 0.4232 | 0.0139 | 0.0172 | 58.48 |
|  |  | CV | 3.0058 | 6.9865 | 6.5983 | 4.8117 | 12.4222 | 6.16 |
| Test_D |  |  |  |  |  |  |  |  |
| Bad PM | 6081 | 6 | 1.5994 | 6.1803 | 6.0125 | 0.3080 |  | 923 |
| MHDTLO | 6082 | 1 | 2.2825 | 8.1942 | 7.7701 | 0.4913 | 0.2156 | 1225 |
|  | 6082 | 2 | 2.3730 | 8.1521 | 7.9994 | 0.4711 | 0.2164 | 1129 |
|  | 6082 | 3 | 2.5827 | 7.7857 | 7.4526 | 0.4899 | 0.2277 | 1216 |
|  |  | Average | 2.4127 | 8.0440 | 7.7407 | 0.4841 | 0.2199 | 1190 |
|  |  | Std Dev | 0.1540 | 0.2246 | 0.2746 | 0.0113 | 0.0068 | 53.16 |
|  |  | CV | 6.3809 | 2.7927 | 3.5478 | 2.3355 | 3.0864 | 4.47 |
| MHDTHI | 6083 | 1 | 1.5813 | 6.3477 | 6.1413 | 0.2979 | 0.2364 | 990 |
|  | 6083 | 2 | 1.7218 | 6.4519 | 6.2065 | 0.3465 | 0.1845 | 1051 |
|  | 6083 | 3 | 1.5599 | 6.3917 | 6.1393 | 0.2982 | 0.1678 | 1017 |
| E55CRC-(truck) | Test ID | Test Run ID | CO g/ahp-hr | NOx1 g/ahp-hr | NOx2 g/ahp-hr | HC g/ahp-hr | PM g/ahp-hr | CO2 g/ahp-hr |
|  |  | Average | 1.6210 | 6.3971 | 6.1624 | 0.3142 | 0.1962 | 1019 |
|  |  | Std Dev | 0.0879 | 0.0523 | 0.0382 | 0.0280 | 0.0358 | 30.57 |
|  |  | CV | 5.4247 | 0.8179 | 0.6201 | 8.9017 | 18.2354 | 3.00 |
| MHDTCR | 6084 | 1 | 1.1852 | 7.5157 | 7.2104 | 0.2519 | 0.1285 | 939 |
|  | 6084 | 2 | 1.1796 | 7.3821 | 7.3375 | 0.2687 | 0.1240 | 937 |
|  | 6084 | 3 | 1.2153 | 7.1931 | 6.9382 | 0.2630 | 0.1268 | 974 |
|  |  | Average | 1.1934 | 7.3636 | 7.1620 | 0.2612 | 0.1264 | 950 |
|  |  | Std Dev | 0.0192 | 0.1621 | 0.2040 | 0.0085 | 0.0022 | 20.83 |
|  |  | CV | 1.6097 | 2.2008 | 2.8483 | 3.2604 | 1.7761 | 2.19 |
| UNLADEN |
| MHDTLO | 6098 | 1 | 3.8488 | 10.8641 | 10.4706 | 0.7352 | 0.3109 | 1556 |
|  | 6099 | 1 | 3.3931 | 10.6189 | 10.3190 | 0.7418 | 0.2486 | 1483 |
|  | 6100 | 1 | 4.1793 | 11.6979 | 11.5123 | 0.7376 | 0.3705 | 1662 |
|  | 6101 | 1 | 4.1059 | 10.6147 | 10.0146 | 0.7084 | 0.2413 | 1506 |
|  |  | Average | 3.8818 | 10.9489 | 10.5791 | 0.7308 | 0.2929 | 1552 |
|  |  | Std Dev | 0.3553 | 0.5128 | 0.6504 | 0.0151 | 0.0605 | 79.79 |
|  |  | CV | 9.1521 | 4.6834 | 6.1478 | 2.0731 | 20.6504 | 5.14 |
| MHDTHI | 6098 | 2 | 1.7241 | 6.1318 | 6.0947 | 0.3465 | 0.2022 | 909 |
|  | 6099 | 2 | 2.0994 | 8.0071 | 7.8216 | 0.4343 | 0.2131 | 1164 |
|  | 6100 | 2 | 2.3381 | 7.7882 | 7.5769 | 0.3785 | 0.2003 | 1149 |
|  | 6101 | 2 | 2.2339 | 7.5270 | 7.4361 | 0.4024 | 0.2010 | 1127 |
|  |  | Average | 2.0989 | 7.3635 | 7.2323 | 0.3904 | 0.2041 | 1087 |
|  |  | Std Dev | 0.2683 | 0.8443 | 0.7750 | 0.0371 | 0.0060 | 120.07 |
|  |  | CV | 12.7824 | 11.4653 | 10.7154 | 9.5139 | 2.9389 | 11.04 |
| MHDTCR | 6098 | 3 | 1.3249 | 7.5092 | 7.1208 | 0.3135 | 0.1641 | 982 |
|  | 6099 | 3 | 1.4694 | 7.4902 | 7.2524 | 0.3128 | 0.1592 | 983 |
|  | 6100 | 3 | 1.6440 | 7.6156 | 7.0847 | 0.3257 | 0.1427 | 1045 |
|  | 6101 | 3 | 1.6146 | 7.3129 | 7.0982 | 0.3293 | 0.1549 | 1026 |
|  |  | Average | 1.5132 | 7.4820 | 7.1391 | 0.3203 | 0.1552 | 1009 |
|  |  | Std Dev | 0.1470 | 0.1255 | 0.0770 | 0.0084 | 0.0092 | 31.65 |
|  |  | CV | 9.7115 | 1.6776 | 1.0791 | 2.6242 | 5.8968 | 3.14 |
| Test_D | 6100 | 4 | 3.1117 | 8.9529 | 9.1239 | 0.5686 | 0.2174 | 1269 |

### TABLE B4: Emissions data from GMC truck (units are g/minute).

| E55CRC-(truck) | Test ID | Test Run ID | CO g/minute | NOx1 g/minute | NOx2 g/minute | HC g/minute | PM g/minute | CO2 g/minute |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LADEN |
| MHDTLO | 6076 | 1 | 0.0075 | 0.0234 | 0.0225 | 0.0014 | 0.000704 | 3.3540 |
|  | 6077 | 1 | 0.0075 | 0.0233 | 0.0224 | 0.0015 | 0.000685 | 3.4451 |
| Bad PM | 6078 | 1 | 0.0073 | 0.0217 | 0.0212 | 0.0014 |  | 3.4278 |
| Bad PM | 6081 | 1 | 0.0070 | 0.0217 | 0.0209 | 0.0014 |  | 3.2202 |
| Bad PM | 6081 | 5 | 0.0062 | 0.0230 | 0.0226 | 0.0012 |  | 3.4705 |
|  | 6104 | 1 | 0.0082 | 0.0235 | 0.0239 | 0.0013 | 0.000761 | 3.4801 |
|  | 6105 | 1 | 0.0080 | 0.0240 | 0.0241 | 0.0013 | 0.000806 | 3.5933 |
|  |  | Average | 0.0078 | 0.0235 | 0.0233 | 0.0014 | 0.000739 | 3.4681 |
|  |  | Std Dev | 0.0003 | 0.0003 | 0.0009 | 0.0001 | 0.000055 | 0.0989 |
|  |  | CV | 4.3895 | 1.4641 | 3.7909 | 7.0203 | 7.460622 | 2.8531 |
| MHDTHI | 6076 | 2 | 0.0353 | 0.1332 | 0.1301 | 0.0071 | 0.004491 | 21.3345 |
|  | 6077 | 2 | 0.0314 | 0.1252 | 0.1230 | 0.0069 | 0.003957 | 21.7194 |
| Bad PM | 6078 | 2 | 0.0325 | 0.1246 | 0.1214 | 0.0070 |  | 20.9417 |
| Bad PM | 6081 | 2 | 0.0320 | 0.1253 | 0.1229 | 0.0066 |  | 20.3288 |
| Bad PM | 6081 | 4 | 0.0297 | 0.1241 | 0.1209 | 0.0058 |  | 19.8773 |
|  | 6104 | 2 | 0.0313 | 0.1260 | 0.1283 | 0.0050 | 0.004104 | 20.2014 |
|  | 6105 | 2 | 0.0300 | 0.1242 | 0.1226 | 0.0053 | 0.003782 | 20.0598 |
|  |  | Average | 0.0320 | 0.1271 | 0.1260 | 0.0061 | 0.004083 | 20.8288 |
|  |  | Std Dev | 0.0023 | 0.0041 | 0.0038 | 0.0011 | 0.000302 | 0.8234 |
|  |  | CV | 7.0566 | 3.2245 | 2.9872 | 18.0373 | 7.399964 | 3.9530 |
| MHDTCR | 6076 | 3 | 0.0523 | 0.2720 | 0.2678 | 0.0122 | 0.005606 | 39.4494 |
|  | 6077 | 3 | 0.0512 | 0.2634 | 0.2584 | 0.0125 | 0.005197 | 38.8466 |
| Bad PM | 6078 | 3 | 0.0526 | 0.2566 | 0.2503 | 0.0111 |  | 37.3623 |
| Bad PM | 6081 | 3 | 0.0514 | 0.2693 | 0.2525 | 0.0105 |  | 37.5136 |
|  | 6104 | 3 | 0.0477 | 0.2642 | 0.2598 | 0.0110 | 0.005846 | 37.9490 |
|  | 6105 | 3 | 0.0476 | 0.2652 | 0.2578 | 0.0116 | 0.005878 | 38.2676 |
|  |  | Average | 0.0497 | 0.2662 | 0.2609 | 0.0118 | 0.005631 | 38.6281 |
|  |  | Std Dev | 0.0024 | 0.0039 | 0.0047 | 0.0006 | 0.000314 | 0.6617 |
|  |  | CV | 4.7992 | 1.4796 | 1.7895 | 5.4787 | 5.581018 | 1.7130 |
| Test_D |  |  |  |  |  |  |  |  |
| Bad PM | 6081 | 6 | 0.0245 | 0.0945 | 0.0920 | 0.0047 |  | 14.1096 |
| MHDTLO | 6082 | 1 | 0.0070 | 0.0250 | 0.0237 | 0.0015 | 0.000659 | 3.7448 |
|  | 6082 | 2 | 0.0074 | 0.0256 | 0.0251 | 0.0015 | 0.000679 | 3.5405 |
|  | 6082 | 3 | 0.0082 | 0.0247 | 0.0236 | 0.0016 | 0.000722 | 3.8521 |
|  |  | Average | 0.0075 | 0.0251 | 0.0242 | 0.0015 | 0.000686 | 3.7125 |
|  |  | Std Dev | 0.0006 | 0.0005 | 0.0008 | 0.0000 | 0.000032 | 0.1583 |
|  |  | CV | 8.0820 | 1.8001 | 3.3813 | 2.5294 | 4.669841 | 4.2645 |
| MHDTHI | 6083 | 1 | 0.0102 | 0.0409 | 0.0395 | 0.0019 | 0.001522 | 6.3714 |
|  | 6083 | 2 | 0.0114 | 0.0427 | 0.0411 | 0.0023 | 0.001221 | 6.9564 |
|  | 6083 | 3 | 0.0102 | 0.0420 | 0.0403 | 0.0020 | 0.001101 | 6.6746 |
| E55CRC-(truck) | Test ID | Test Run ID | CO g/minute | NOx1 g/minute | NOx2 g/minute | HC g/minute | PM g/minute | CO2 g/minute |
|  |  | Average | 0.0106 | 0.0419 | 0.0403 | 0.0021 | 0.001282 | 6.6675 |
|  |  | Std Dev | 0.0007 | 0.0009 | 0.0008 | 0.0002 | 0.000217 | 0.2926 |
|  |  | CV | 6.4767 | 2.2249 | 1.9286 | 10.0482 | 16.894946 | 4.3878 |
| MHDTCR | 6084 | 1 | 0.0093 | 0.0590 | 0.0566 | 0.0020 | 0.001009 | 7.3776 |
|  | 6084 | 2 | 0.0092 | 0.0577 | 0.0574 | 0.0021 | 0.000970 | 7.3260 |
|  | 6084 | 3 | 0.0092 | 0.0547 | 0.0528 | 0.0020 | 0.000964 | 7.4072 |
|  |  | Average | 0.0093 | 0.0572 | 0.0556 | 0.0020 | 0.000981 | 7.3703 |
|  |  | Std Dev | 0.0000 | 0.0022 | 0.0025 | 0.0001 | 0.000024 | 0.0411 |
|  |  | CV | 0.4704 | 3.8838 | 4.4617 | 3.2333 | 2.477652 | 0.5573 |
| UNLADEN |
| MHDTLO | 6098 | 1 | 0.0078 | 0.0221 | 0.0213 | 0.0015 | 0.000633 | 3.1679 |
|  | 6099 | 1 | 0.0068 | 0.0213 | 0.0207 | 0.0015 | 0.000499 | 2.9748 |
|  | 6100 | 1 | 0.0082 | 0.0229 | 0.0225 | 0.0014 | 0.000725 | 3.2514 |
|  | 6101 | 1 | 0.0083 | 0.0214 | 0.0202 | 0.0014 | 0.000487 | 3.0375 |
|  |  | Average | 0.0078 | 0.0219 | 0.0212 | 0.0015 | 0.000586 | 3.1079 |
|  |  | Std Dev | 0.0007 | 0.0007 | 0.0010 | 0.0000 | 0.000114 | 0.1250 |
|  |  | CV | 8.6534 | 3.3279 | 4.7144 | 2.2646 | 19.435325 | 4.0213 |
| MHDTHI | 6098 | 2 | 0.0341 | 0.1212 | 0.1205 | 0.0068 | 0.003997 | 17.9582 |
|  | 6099 | 2 | 0.0302 | 0.1152 | 0.1125 | 0.0062 | 0.003064 | 16.7393 |
|  | 6100 | 2 | 0.0331 | 0.1102 | 0.1072 | 0.0054 | 0.002833 | 16.2565 |
|  | 6101 | 2 | 0.0320 | 0.1080 | 0.1067 | 0.0058 | 0.002883 | 16.1727 |
|  |  | Average | 0.0323 | 0.1136 | 0.1117 | 0.0061 | 0.003194 | 16.7817 |
|  |  | Std Dev | 0.0017 | 0.0059 | 0.0064 | 0.0006 | 0.000544 | 0.8231 |
|  |  | CV | 5.1246 | 5.1685 | 5.7336 | 10.6130 | 17.036006 | 4.9050 |
| MHDTCR | 6098 | 3 | 0.0489 | 0.2772 | 0.2629 | 0.0116 | 0.006058 | 36.2447 |
|  | 6099 | 3 | 0.0529 | 0.2695 | 0.2609 | 0.0113 | 0.005728 | 35.3487 |
|  | 6100 | 3 | 0.0587 | 0.2720 | 0.2530 | 0.0116 | 0.005097 | 37.3201 |
|  | 6101 | 3 | 0.0575 | 0.2602 | 0.2526 | 0.0117 | 0.005512 | 36.4941 |
|  |  | Average | 0.0545 | 0.2697 | 0.2574 | 0.0115 | 0.005599 | 36.3519 |
|  |  | Std Dev | 0.0045 | 0.0071 | 0.0053 | 0.0002 | 0.000403 | 0.8115 |
|  |  | CV | 8.2398 | 2.6305 | 2.0615 | 1.7468 | 7.196336 | 2.2323 |
| Test_D | 6100 | 4 | 0.0317 | 0.0911 | 0.0929 | 0.0058 | 0.002213 | 12.9142 |

### TABLE B5: Emissions data from GMC truck (units are g/gallon).

| E55CRC-(truck) | Test ID | Test Run ID | CO (g/gallon) | NOx1 (g/gallon) | NOx2 (g/gallon) | HC (g/gallon) | PM (g/gallon) | GALLON |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| LADEN |
| MHDTLO | 6076 | 1 | 22.4987 | 69.6235 | 67.1894 | 4.1623 | 2.0993 | 0.1174 |
|  | 6077 | 1 | 21.8085 | 67.5275 | 65.1608 | 4.3063 | 1.9886 | 0.1206 |
| Bad PM | 6078 | 1 | 21.3964 | 63.2065 | 61.8431 | 4.0136 |  | 0.1200 |
| Bad PM | 6081 | 1 | 21.8223 | 67.5060 | 64.8000 | 4.3494 |  | 0.1127 |
| Bad PM | 6081 | 5 | 17.7731 | 66.3806 | 65.1627 | 3.5510 |  | 0.1214 |
|  | 6104 | 1 | 23.5614 | 67.6065 | 68.6427 | 3.6727 | 2.1875 | 0.1218 |
|  | 6105 | 1 | 22.3225 | 66.8985 | 67.1545 | 3.6037 | 2.2437 | 0.1258 |
|  |  | Average | 22.5478 | 67.9140 | 67.0369 | 3.9363 | 2.1298 | 0.1214 |
|  |  | Std Dev | 0.7365 | 1.1828 | 1.4301 | 0.3503 | 0.1113 | 0.0035 |
|  |  | CV | 3.2662 | 1.7417 | 2.1333 | 8.8986 | 5.2261 | 2.8449 |
| MHDTHI | 6076 | 2 | 16.5540 | 62.5053 | 61.0691 | 3.3337 | 2.1075 | 0.7459 |
|  | 6077 | 2 | 14.4991 | 57.7232 | 56.7338 | 3.1851 | 1.8245 | 0.7591 |
| Bad PM | 6078 | 2 | 15.5211 | 59.5912 | 58.0596 | 3.3276 |  | 0.7320 |
| Bad PM | 6081 | 2 | 15.7688 | 61.7153 | 60.5097 | 3.2383 |  | 0.7106 |
| Bad PM | 6081 | 4 | 14.9728 | 62.5375 | 60.9042 | 2.9338 |  | 0.6947 |
|  | 6104 | 2 | 15.5324 | 62.4487 | 63.6015 | 2.4680 | 2.0348 | 0.7060 |
|  | 6105 | 2 | 15.0016 | 62.0293 | 61.2280 | 2.6349 | 1.8881 | 0.7010 |
|  |  | Average | 15.3968 | 61.1766 | 60.6581 | 2.9054 | 1.9637 | 0.7280 |
|  |  | Std Dev | 0.8793 | 2.3120 | 2.8611 | 0.4188 | 0.1302 | 0.0289 |
|  |  | CV | 5.7109 | 3.7793 | 4.7167 | 14.4142 | 6.6285 | 3.9650 |
| MHDTCR | 6076 | 3 | 13.2725 | 69.0685 | 68.0081 | 3.0870 | 1.4234 | 1.3784 |
|  | 6077 | 3 | 13.1960 | 67.9229 | 66.6272 | 3.2134 | 1.3400 | 1.3574 |
| Bad PM | 6078 | 3 | 14.1099 | 68.7798 | 67.1025 | 2.9786 |  | 1.3056 |
| Bad PM | 6081 | 3 | 13.7335 | 71.9173 | 67.4331 | 2.8117 |  | 1.3107 |
|  | 6104 | 3 | 12.5947 | 69.7409 | 68.5748 | 2.9016 | 1.5433 | 1.3257 |
|  | 6105 | 3 | 12.4683 | 69.4397 | 67.4861 | 3.0409 | 1.5387 | 1.3369 |
|  |  | Average | 12.8828 | 69.0430 | 67.6740 | 3.0607 | 1.4613 | 1.3496 |
|  |  | Std Dev | 0.4102 | 0.7958 | 0.8275 | 0.1288 | 0.0981 | 0.0232 |
|  |  | CV | 3.1840 | 1.1526 | 1.2227 | 4.2065 | 6.7153 | 1.7215 |
| Test_D |  |  |  |  |  |  |  |  |
| Bad PM | 6081 | 6 | 17.3545 | 67.0605 | 65.2397 | 3.3425 |  | 0.4934 |
| MHDTLO | 6082 | 1 | 18.6399 | 66.9161 | 63.4530 | 4.0123 | 1.7605 | 0.1310 |
|  | 6082 | 2 | 21.0268 | 72.2330 | 70.8805 | 4.1740 | 1.9176 | 0.1239 |
|  | 6082 | 3 | 21.2482 | 64.0552 | 61.3141 | 4.0307 | 1.8736 | 0.1348 |
|  |  | Average | 20.3050 | 67.7348 | 65.2159 | 4.0723 | 1.8505 | 0.1299 |
|  |  | Std Dev | 1.4462 | 4.1499 | 5.0209 | 0.0886 | 0.0810 | 0.0055 |
|  |  | CV | 7.1226 | 6.1266 | 7.6990 | 2.1746 | 4.3793 | 4.2603 |
| MHDTHI | 6083 | 1 | 15.9998 | 64.2268 | 62.1390 | 3.0139 | 2.3915 | 0.7445 |
|  | 6083 | 2 | 16.4072 | 61.4813 | 59.1426 | 3.3017 | 1.7578 | 0.8130 |
|  | 6083 | 3 | 15.3671 | 62.9659 | 60.4798 | 2.9377 | 1.6526 | 0.7798 |
| E55CRC-(truck) | Test ID | Test Run ID | CO (g/gallon) | NOx1 (g/gallon) | NOx2 (g/gallon) | HC (g/gallon) | PM (g/gallon) | GALLON |
|  |  | Average | 15.9247 | 62.8913 | 60.5871 | 3.0844 | 1.9340 | 0.7791 |
|  |  | Std Dev | 0.5241 | 1.3743 | 1.5011 | 0.1920 | 0.3997 | 0.0342 |
|  |  | CV | 3.2910 | 2.1852 | 2.4776 | 6.2233 | 20.6699 | 4.3956 |
| MHDTCR | 6084 | 1 | 12.6403 | 80.1553 | 76.8997 | 2.6870 | 1.3703 | 1.3917 |
|  | 6084 | 2 | 12.6162 | 78.9543 | 78.4778 | 2.8737 | 1.3267 | 1.3820 |
|  | 6084 | 3 | 12.5007 | 73.9884 | 71.3663 | 2.7057 | 1.3044 | 1.3973 |
|  |  | Average | 12.5857 | 77.6993 | 75.5813 | 2.7555 | 1.3338 | 1.3903 |
|  |  | Std Dev | 0.0746 | 3.2694 | 3.7346 | 0.1028 | 0.0335 | 0.0077 |
|  |  | CV | 0.5931 | 4.2077 | 4.9411 | 3.7313 | 2.5140 | 0.5536 |
| UNLADEN |
| MHDTLO | 6098 | 1 | 24.7147 | 69.7630 | 67.2361 | 4.7209 | 1.9965 | 0.1109 |
|  | 6099 | 1 | 22.8758 | 71.5913 | 69.5692 | 5.0014 | 1.6763 | 0.1042 |
|  | 6100 | 1 | 25.1303 | 70.3408 | 69.2246 | 4.4354 | 2.2281 | 0.1139 |
|  | 6101 | 1 | 27.2448 | 70.4336 | 66.4515 | 4.7007 | 1.6013 | 0.1064 |
|  |  | Average | 24.9914 | 70.5322 | 68.1203 | 4.7146 | 1.8756 | 0.1088 |
|  |  | Std Dev | 1.7934 | 0.7659 | 1.5150 | 0.2312 | 0.2909 | 0.0044 |
|  |  | CV | 7.1762 | 1.0859 | 2.2240 | 4.9048 | 15.5093 | 4.0198 |
| MHDTHI | 6098 | 2 | 18.9858 | 67.5247 | 67.1152 | 3.8161 | 2.2269 | 0.6282 |
|  | 6099 | 2 | 18.0505 | 68.8449 | 67.2500 | 3.7343 | 1.8319 | 0.5854 |
|  | 6100 | 2 | 20.3543 | 67.7996 | 65.9597 | 3.2948 | 1.7438 | 0.5687 |
|  | 6101 | 2 | 19.8256 | 66.8025 | 65.9960 | 3.5712 | 1.7835 | 0.5658 |
|  |  | Average | 19.3041 | 67.7429 | 66.5802 | 3.6041 | 1.8965 | 0.5870 |
|  |  | Std Dev | 1.0079 | 0.8465 | 0.6979 | 0.2299 | 0.2232 | 0.0288 |
|  |  | CV | 5.2213 | 1.2496 | 1.0482 | 6.3797 | 11.7693 | 4.9030 |
| MHDTCR | 6098 | 3 | 13.5153 | 76.6037 | 72.6419 | 3.1977 | 1.6742 | 1.2665 |
|  | 6099 | 3 | 14.9763 | 76.3416 | 73.9184 | 3.1884 | 1.6226 | 1.2355 |
|  | 6100 | 3 | 15.7532 | 72.9735 | 67.8866 | 3.1208 | 1.3675 | 1.3045 |
|  | 6101 | 3 | 15.7640 | 71.3996 | 69.3042 | 3.2147 | 1.5122 | 1.2757 |
|  |  | Average | 15.0022 | 74.3296 | 70.9378 | 3.1804 | 1.5441 | 1.2705 |
|  |  | Std Dev | 1.0577 | 2.5589 | 2.8146 | 0.0412 | 0.1357 | 0.0284 |
|  |  | CV | 7.0500 | 3.4426 | 3.9677 | 1.2957 | 8.7909 | 2.2382 |
| Test_D | 6100 | 4 | 24.5115 | 70.5236 | 71.8706 | 4.4787 | 1.7125 | 0.4522 |

### TABLE B6: Emissions data from the automatic Freightliner truck (units are g/cycle).

| Driving Schedule | Test ID | Test Run ID | CO (g/cycle) | NOx1 (g/cycle) | NOx2 (g/cycle) | HC (g/cycle) | PM (g/cycle) | CO2 (g/cycle) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MHDTLO | 6108 | 3 | 3.4925 | 16.2598 | 16.2043 | 0.4903 | 0.3266 | 1612.66 |
| MHDTLO | 6108 | 4 | 3.3606 | 15.8553 | 15.8793 | 0.4626 | 0.3355 | 1613.74 |
| MHDTLO | 6108 | 5 | 3.4988 | 15.7337 | 15.3851 | 0.4658 | 0.3097 | 1625.48 |
|  |  | Average | 3.4506 | 15.9496 | 15.8229 | 0.4729 | 0.3239 | 1617.29 |
|  |  | Std Dev | 0.0780 | 0.2754 | 0.4125 | 0.0151 | 0.0131 | 7.11 |
|  |  | CV | 2.2609 | 1.7269 | 2.6069 | 3.2027 | 4.0544 | 0.44 |
| MHDTHI | 6109 | 1 | 13.5576 | 92.2127 | 90.4380 | 2.5193 | 1.8360 | 8887.74 |
| MHDTHI | 6109 | 2 | 13.7513 | 90.2182 | 89.7025 | 2.5517 | 1.7960 | 8809.70 |
| MHDTHI | 6109 | 3 | 14.3164 | 89.7935 | 87.0235 | 2.3910 | 1.6890 | 8720.64 |
|  |  | Average | 13.8751 | 90.7414 | 89.0547 | 2.4873 | 1.7736 | 8806.02 |
|  |  | Std Dev | 0.3943 | 1.2917 | 1.7971 | 0.0850 | 0.0760 | 83.61 |
|  |  | CV | 2.8415 | 1.4235 | 2.0180 | 3.4173 | 4.2848 | 0.95 |
| MHDTCR | 6112 | 1 | 25.5837 | 175.4095 | 171.5174 | 7.5218 | 2.6447 | 24089.49 |
| MHDTCR | 6112 | 2 | 24.5086 | 163.0709 | 163.3274 | 7.2748 | 3.3254 | 23235.38 |
| MHDTCR | 6112 | 3 | 26.0715 | 167.1607 | 167.4605 | 6.8611 | 3.0452 | 22925.89 |
|  |  | Average | 25.3879 | 168.5471 | 167.4351 | 7.2192 | 3.0051 | 23416.92 |
|  |  | Std Dev | 0.7997 | 6.2850 | 4.0950 | 0.3338 | 0.3421 | 602.67 |
|  |  | CV | 3.1497 | 3.7289 | 2.4457 | 4.6243 | 11.3848 | 2.57 |
| TEST_D | 6113 | 3 | 11.8090 | 41.5927 | 41.6216 | 2.7923 | 1.1051 | 7045.95 |
| TEST_D | 6113 | 4 | 11.0523 | 42.9860 | 43.4707 | 2.7222 | 1.1041 | 6904.51 |
| TEST_D | 6113 | 5 | 11.0468 | 41.6402 | 41.8969 | 2.9198 | 0.9493 | 7062.27 |
|  |  | Average | 11.3027 | 42.0730 | 42.3297 | 2.8114 | 1.0528 | 7004.24 |
|  |  | Std Dev | 0.4385 | 0.7911 | 0.9976 | 0.1002 | 0.0897 | 86.76 |
|  |  | CV | 3.8797 | 1.8802 | 2.3568 | 3.5625 | 8.5193 | 1.24 |

### TABLE B7: Emissions data from the automatic Freightliner truck (units are g/mile).

| Driving Schedule | Test ID | Test Run ID | CO (g/mile) | NOx1 (g/mile) | NOx2 (g/mile) | HC (g/mile) | PM (g/mile) | CO2 (g/mile) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MHDTLO | 6108 | 3 | 3.5691 | 16.6168 | 16.5601 | 0.5010 | 0.3338 | 1648.07 |
| MHDTLO | 6108 | 4 | 3.4512 | 16.2828 | 16.3074 | 0.4750 | 0.3445 | 1657.25 |
| MHDTLO | 6108 | 5 | 3.6205 | 16.2810 | 15.9203 | 0.4820 | 0.3204 | 1682.03 |
|  |  | Average | 3.5469 | 16.3935 | 16.2626 | 0.4860 | 0.3329 | 1662.45 |
|  |  | Std Dev | 0.0868 | 0.1934 | 0.3222 | 0.0135 | 0.0121 | 17.57 |
|  |  | CV | 2.4468 | 1.1795 | 1.9815 | 2.7682 | 3.6298 | 1.06 |
| MHDTHI | 6109 | 1 | 1.8891 | 12.8490 | 12.6017 | 0.3510 | 0.2558 | 1238.43 |
| MHDTHI | 6109 | 2 | 1.9057 | 12.5025 | 12.4310 | 0.3536 | 0.2489 | 1220.85 |
| MHDTHI | 6109 | 3 | 1.9820 | 12.4313 | 12.0478 | 0.3310 | 0.2338 | 1207.31 |
|  |  | Average | 1.9256 | 12.5943 | 12.3602 | 0.3452 | 0.2462 | 1222.20 |
|  |  | Std Dev | 0.0495 | 0.2235 | 0.2837 | 0.0124 | 0.0112 | 15.60 |
|  |  | CV | 2.5729 | 1.7744 | 2.2951 | 3.5841 | 4.5683 | 1.28 |
| MHDTCR | 6112 | 1 | 1.2040 | 8.2549 | 8.0717 | 0.3540 | 0.1245 | 1133.67 |
| MHDTCR | 6112 | 2 | 1.1534 | 7.6743 | 7.6863 | 0.3424 | 0.1565 | 1093.48 |
| MHDTCR | 6112 | 3 | 1.2254 | 7.8570 | 7.8711 | 0.3225 | 0.1431 | 1077.58 |
|  |  | Average | 1.1943 | 7.9287 | 7.8764 | 0.3396 | 0.1414 | 1101.57 |
|  |  | Std Dev | 0.0370 | 0.2969 | 0.1928 | 0.0159 | 0.0161 | 28.91 |
|  |  | CV | 3.0971 | 3.7445 | 2.4473 | 4.6892 | 11.3825 | 2.62 |
| TEST_D | 6113 | 3 | 2.1254 | 7.4860 | 7.4912 | 0.5026 | 0.1989 | 1268.16 |
| TEST_D | 6113 | 4 | 1.9914 | 7.7454 | 7.8327 | 0.4905 | 0.1989 | 1244.08 |
| TEST_D | 6113 | 5 | 1.9865 | 7.4882 | 7.5343 | 0.5251 | 0.1707 | 1270.01 |
|  |  | Average | 2.0345 | 7.5732 | 7.6194 | 0.5060 | 0.1895 | 1260.75 |
|  |  | Std Dev | 0.0788 | 0.1491 | 0.1860 | 0.0175 | 0.0163 | 14.46 |
|  |  | CV | 3.8739 | 1.9692 | 2.4408 | 3.4665 | 8.5962 | 1.15 |

### TABLE B8: Emissions data from the automatic Freightliner truck (units are

### g/ahp-hr).

| Driving Schedule | Test ID | Test Run ID | CO g/ahp-hr | NOx1 g/ahp-hr | NOx2 g/ahp-hr | HC g/ahp-hr | PM g/ahp-hr | CO2 g/ahp-hr |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MHDTLO | 6108 | 3 | 4.0535 | 18.8716 | 18.8073 | 0.5690 | 0.3791 | 1871.70 |
| MHDTLO | 6108 | 4 | 3.9177 | 18.4835 | 18.5114 | 0.5392 | 0.3911 | 1881.24 |
| MHDTLO | 6108 | 5 | 4.0757 | 18.3282 | 17.9222 | 0.5426 | 0.3607 | 1893.52 |
|  |  | Average | 4.0156 | 18.5611 | 18.4136 | 0.5503 | 0.3770 | 1882.15 |
|  |  | Std Dev | 0.0856 | 0.2799 | 0.4506 | 0.0163 | 0.0153 | 10.94 |
|  |  | CV | 2.1306 | 1.5081 | 2.4471 | 2.9631 | 4.0612 | 0.58 |
| MHDTHI | 6109 | 1 | 2.1995 | 14.9602 | 14.6723 | 0.4087 | 0.2979 | 1441.91 |
| MHDTHI | 6109 | 2 | 2.2378 | 14.6814 | 14.5974 | 0.4152 | 0.2923 | 1433.62 |
| MHDTHI | 6109 | 3 | 2.3491 | 14.7338 | 14.2793 | 0.3923 | 0.2771 | 1430.93 |
|  |  | Average | 2.2621 | 14.7918 | 14.5164 | 0.4054 | 0.2891 | 1435.49 |
|  |  | Std Dev | 0.0777 | 0.1482 | 0.2087 | 0.0118 | 0.0107 | 5.72 |
|  |  | CV | 3.4355 | 1.0018 | 1.4374 | 2.9125 | 3.7082 | 0.40 |
| MHDTCR | 6112 | 1 | 1.6346 | 11.2072 | 10.9585 | 0.4806 | 0.1690 | 1539.12 |
| MHDTCR | 6112 | 2 | 1.5741 | 10.4735 | 10.4899 | 0.4672 | 0.2136 | 1492.33 |
| MHDTCR | 6112 | 3 | 1.6923 | 10.8503 | 10.8698 | 0.4454 | 0.1977 | 1488.11 |
|  |  | Average | 1.6337 | 10.8437 | 10.7728 | 0.4644 | 0.1934 | 1506.52 |
|  |  | Std Dev | 0.0591 | 0.3669 | 0.2489 | 0.0178 | 0.0226 | 28.31 |
|  |  | CV | 3.6178 | 3.3837 | 2.3106 | 3.8300 | 11.6880 | 1.88 |
| TEST_D | 6113 | 3 | 2.7934 | 9.8388 | 9.8456 | 0.6605 | 0.2614 | 1666.72 |
| TEST_D | 6113 | 4 | 2.6922 | 10.4708 | 10.5888 | 0.6631 | 0.2690 | 1681.84 |
| TEST_D | 6113 | 5 | 2.6678 | 10.0561 | 10.1181 | 0.7051 | 0.2293 | 1705.53 |
|  |  | Average | 2.7178 | 10.1219 | 10.1842 | 0.6762 | 0.2532 | 1684.70 |
|  |  | Std Dev | 0.0666 | 0.3211 | 0.3760 | 0.0250 | 0.0211 | 19.56 |
|  |  | CV | 2.4514 | 3.1722 | 3.6919 | 3.7033 | 8.3279 | 1.16 |

### TABLE B9: Emissions data from the automatic Freightliner truck (units are g/minute).

| Driving Schedule | Test ID | Test Run ID | CO g/minute | NOx1 g/minute | NOx2 g/minute | HC g/minute | PM g/minute | CO2 g/minute |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MHDTLO | 6108 | 3 | 0.0100 | 0.0465 | 0.0463 | 0.0014 | 0.000933 | 4.6076 |
| MHDTLO | 6108 | 4 | 0.0096 | 0.0453 | 0.0454 | 0.0013 | 0.000959 | 4.6107 |
| MHDTLO | 6108 | 5 | 0.0100 | 0.0450 | 0.0440 | 0.0013 | 0.000885 | 4.6442 |
|  |  | Average | 0.0099 | 0.0456 | 0.0452 | 0.0014 | 0.000926 | 4.6208 |
|  |  | Std Dev | 0.0002 | 0.0008 | 0.0012 | 0.0000 | 0.000038 | 0.0203 |
|  |  | CV | 2.2609 | 1.7269 | 2.6069 | 3.2027 | 4.054422 | 0.4398 |
| MHDTHI | 6109 | 1 | 0.0116 | 0.0788 | 0.0773 | 0.0022 | 0.001569 | 7.5964 |
| MHDTHI | 6109 | 2 | 0.0118 | 0.0771 | 0.0767 | 0.0022 | 0.001535 | 7.5297 |
| MHDTHI | 6109 | 3 | 0.0122 | 0.0767 | 0.0744 | 0.0020 | 0.001444 | 7.4535 |
|  |  | Average | 0.0119 | 0.0776 | 0.0761 | 0.0021 | 0.001516 | 7.5265 |
|  |  | Std Dev | 0.0003 | 0.0011 | 0.0015 | 0.0001 | 0.000065 | 0.0715 |
|  |  | CV | 2.8415 | 1.4235 | 2.0180 | 3.4173 | 4.284848 | 0.9495 |
| MHDTCR | 6112 | 1 | 0.0135 | 0.0928 | 0.0907 | 0.0040 | 0.001399 | 12.7458 |
| MHDTCR | 6112 | 2 | 0.0130 | 0.0863 | 0.0864 | 0.0038 | 0.001759 | 12.2939 |
| MHDTCR | 6112 | 3 | 0.0138 | 0.0884 | 0.0886 | 0.0036 | 0.001611 | 12.1301 |
|  |  | Average | 0.0134 | 0.0892 | 0.0886 | 0.0038 | 0.001590 | 12.3899 |
|  |  | Std Dev | 0.0004 | 0.0033 | 0.0022 | 0.0002 | 0.000181 | 0.3189 |
|  |  | CV | 3.1497 | 3.7289 | 2.4457 | 4.6243 | 11.384763 | 2.5736 |
| TEST_D | 6113 | 3 | 0.0114 | 0.0400 | 0.0400 | 0.0027 | 0.001063 | 6.7750 |
| TEST_D | 6113 | 4 | 0.0106 | 0.0413 | 0.0418 | 0.0026 | 0.001062 | 6.6390 |
| TEST_D | 6113 | 5 | 0.0106 | 0.0400 | 0.0403 | 0.0028 | 0.000913 | 6.7906 |
|  |  | Average | 0.0109 | 0.0405 | 0.0407 | 0.0027 | 0.001012 | 6.7348 |
|  |  | Std Dev | 0.0004 | 0.0008 | 0.0010 | 0.0001 | 0.000086 | 0.0834 |
|  |  | CV | 3.8797 | 1.8802 | 2.3568 | 3.5625 | 8.519319 | 1.2386 |

### TABLE B10: Emissions data from the automatic Freightliner truck (units are g/gallon).

| Driving Schedule | Test ID | Test Run ID | CO g/gallon | NOx1 g/gallon | NOx2 g/gallon | HC g/gallon | PM g/gallon | GALLON |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MHDTLO | 6108 | 3 | 21.6650 | 100.8655 | 100.5216 | 3.0412 | 2.0262 | 0.1612 |
| MHDTLO | 6108 | 4 | 20.8370 | 98.3084 | 98.4573 | 2.8680 | 2.0802 | 0.1613 |
| MHDTLO | 6108 | 5 | 21.5346 | 96.8393 | 94.6941 | 2.8669 | 1.9059 | 0.1625 |
|  |  | Average | 21.3455 | 98.6711 | 97.8910 | 2.9254 | 2.0041 | 0.1617 |
|  |  | Std Dev | 0.4452 | 2.0375 | 2.9547 | 0.1003 | 0.0892 | 0.0007 |
|  |  | CV | 2.0858 | 2.0649 | 3.0184 | 3.4297 | 4.4531 | 0.4401 |
| MHDTHI | 6109 | 1 | 15.2765 | 103.9043 | 101.9046 | 2.8387 | 2.0688 | 0.8875 |
| MHDTHI | 6109 | 2 | 15.6309 | 102.5497 | 101.9635 | 2.9005 | 2.0415 | 0.8798 |
| MHDTHI | 6109 | 3 | 16.4381 | 103.1013 | 99.9208 | 2.7453 | 1.9393 | 0.8709 |
|  |  | Average | 15.7819 | 103.1851 | 101.2630 | 2.8282 | 2.0165 | 0.8794 |
|  |  | Std Dev | 0.5953 | 0.6812 | 1.1627 | 0.0781 | 0.0682 | 0.0083 |
|  |  | CV | 3.7723 | 0.6602 | 1.1482 | 2.7620 | 3.3842 | 0.9418 |
| MHDTCR | 6112 | 1 | 10.6426 | 72.9685 | 71.3494 | 3.1290 | 1.1002 | 2.4039 |
| MHDTCR | 6112 | 2 | 10.5702 | 70.3299 | 70.4406 | 3.1375 | 1.4342 | 2.3187 |
| MHDTCR | 6112 | 3 | 11.3951 | 73.0608 | 73.1918 | 2.9988 | 1.3310 | 2.2880 |
|  |  | Average | 10.8693 | 72.1197 | 71.6606 | 3.0884 | 1.2884 | 2.3368 |
|  |  | Std Dev | 0.4568 | 1.5507 | 1.4018 | 0.0778 | 0.1710 | 0.0601 |
|  |  | CV | 4.2025 | 2.1502 | 1.9561 | 2.5175 | 13.2739 | 2.5707 |
| TEST_D | 6113 | 3 | 16.7746 | 59.0819 | 59.1229 | 3.9664 | 1.5698 | 0.7040 |
| TEST_D | 6113 | 4 | 16.0232 | 62.3196 | 63.0223 | 3.9466 | 1.6008 | 0.6898 |
| TEST_D | 6113 | 5 | 15.6575 | 59.0198 | 59.3837 | 4.1384 | 1.3455 | 0.7055 |
|  |  | Average | 16.1518 | 60.1404 | 60.5096 | 4.0171 | 1.5053 | 0.6998 |
|  |  | Std Dev | 0.5695 | 1.8875 | 2.1800 | 0.1055 | 0.1393 | 0.0087 |
|  |  | CV | 3.5261 | 3.1385 | 3.6027 | 2.6263 | 9.2543 | 1.2417 |